## Slide 1
www.technologystudent.com © 2018
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
V.Ryan © 2018
www.technologystudent.com © 2018
https://www.facebook.com/groups/254963448192823/
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
V.Ryan © 2018
DESIGN AND TECHNOLOGY - THE NEA

## Slide 2
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018
www.technologystudent.com provides all your needs for the delivery of the New Design and Technology GCSE. Free to access - but please respect the copyright
IMPORTANT LINKS - FOR A SUCCESSFUL DELIVERY OF THE COURSE
ITERATIVE DESIGN AND THE NEA
http://www.technologystudent.com/designpro/despro1.htm
DETAILED CONTENT AND EXERCISES FOLLOWING THE GCSE SPECIFICATION
http://www.technologystudent.com/despro_ﬂsh/new_maths1.html DESIGNERS, DESIGN MOVEMENTS AND COMPANIES
http://www.technologystudent.com/despro_ﬂsh/Designer1.html MATERIALS, EQUIPMENT AND INDUSTRIAL PROCESSES
http://www.technologystudent.com/despro_ﬂsh/materials_main1.html http://www.technologystudent.com/equip1/equipex1.htm
GRAPHICS, DRAWING TECHNIQUES AND INDUSTRIAL PROCESSES
http://www.technologystudent.com/despro_ﬂsh/graphics_main1.html MATHEMATICS AND DESIGN AND TECHNOLOGY
http://www.technologystudent.com/despro_ﬂsh/new_maths1.html TOTAL REVISION - FOR EXAMINATIONS
http://www.technologystudent.com/despro_ﬂsh/new_revison1.html http://www.technologystudent.com/despro_ﬂsh/vid_channel2.html

## Slide 3
A GUIDE TO
THE NON-EXAM ASSESSMENT
NEA
50% OF TOTAL MARKS OF THE GCSE
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018
COPYRIGHT STATEMENT
This PowerPoint / pdf can be duplicated and printed out if required, but not edited in any way.
The links to www.technologystudent.com cannot be removed.
The PDF and PowerPoint ﬁles can be stored on school / college systems and distributed electronically (NO EDITING ALLOWED). Absolutely NO copying in part or whole.
PLEASE RESPECT THE COPYRIGHT - report infringers to techteacher@technologystudent.com Not be distributed at courses or by course instructors / consultants
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 4
The NEA is a single task that contributes 50% of all marks for the Design and Technology GCSE.
Students will be given a choice of a number of Contextual Challenges (themes). They will research and investigate one or more of these themes, in order to ﬁnd a design problem to solve.
Students will consider the design problem, from the point of view of a potential client / customer, leading to a design brief and speciﬁcation. Then, they will produce a series of designs and develop one or more, leading to a ﬁnal manufactured prototype. This will be fully tested and evaluated.
Students will produce a portfolio (written or digital), of approximately twenty design sheets. Examination boards recommend that students do not exceed twenty sheets and spend between 30 to 35 hours on the NEA, which includes the manufacture of the ﬁnal prototype.
www.technologystudent.com © 2018 V.Ryan © 2018
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
https://www.facebook.com/groups/254963448192823/
https://www.facebook.com/groups/254963448192823/
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 5
PLEASE NOTE:
IT IS THE TEACHERS RESPONSIBILITY TO FOLLOW ALL REGULATIONS AND GUIDANCE FROM THE EXAMINATION BOARDS. THIS PRESENTATION / DOCUMENT IS MY INTERPRETATION.
PLEASE READ THE FOLLOWING:
The appropriate examination board specification.
AND ESPECIALLY:
Instructions for conducting non-examination assessments 2017-2018
https://www.jcq.org.uk/exams-office/non-examination-assessments/in

## Slide 6
HELP THE TEACHER CAN and CANNOT GIVE TO STUDENTS
Teachers cannot give students direct help or personalised feedback. This includes correcting student work and giving speciﬁc sample answers.
Teachers cannot tell students how to improve their work, in order to achieve better marks (according to the marking criteria).
Teachers can give generic feedback (general advice). This could include the following (read your specification): Advice on the resources that could be used.
If a student has missed out an important section, the teacher can draw this to the student’s attention.
Teachers can explain key words and phrases, that students may not be sure about.
There are a variety of ways of providing classes with ‘generic’ feedback.
SUMMARY - TEACHERS CAN GIVE ONLY GENERIC ADVICE NOT PORTFOLIO OR STUDENT SPECIFIC ADVICE.
www.technologystudent.com © 2018 V.Ryan © 2018
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
https://www.facebook.com/groups/254963448192823/
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018
YOU MUST READ YOUR SPECIFICATION FOR DETAILED GUIDANCE

## Slide 7
THE SLIDES THAT FOLLOW WILL PROVIDE GENERAL / GENERIC ADVICE.
THE SLIDES DESCRIBE WAYS STUDENTS CAN PROGRESS THROUGH THE NEA.
SAMPLE PAGES FROM A RANGE OF PROJECTS ARE USED THROUGHOUT THIS POWERPOINT, TO SUPPORT THE INDEPENDENT WORK OF STUDENTS.
www.technologystudent.com © 2018 V.Ryan © 2018
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018
https://www.facebook.com/groups/254963448192823/
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
V.Ryan © 2018

## Slide 8
WHAT IS ITERATIVE DESIGN?
HOW IT CAN BE APPLIED TO THE NEA?
www.technologystudent.com © 2018 V.Ryan © 2018
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
https://www.facebook.com/groups/254963448192823/
HELPFUL LINK http://www.technologystudent.com/despro_ﬂsh/iterative1.html
https://www.facebook.com/groups/254963448192823/
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 9
HOW ITERATIVE DESIGN WORKS
Iterative design is the process of continual improvement, of a concept, prototype, design or product. It is a CYCLICAL approach to the development of a product, whereby a design is improved by frequent testing, client feedback, focus groups, materials testing, prototype testing, design development and evaluation, until a ﬁnal reﬁned / developed design/product is reached.
It diﬀers from the linear approach to design, whereby the designer goes through a number of predeﬁned stages, one at a time, until a conclusive design is reached.
The Iterative Design Cycle works at it’s best, when a student understands how each of it’s individual components (we call them ‘DESIGN TOOLS’) can be used, to help in the design and development of a product.
www.technologystudent.com © 2018 V.Ryan © 2018
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
https://www.facebook.com/groups/254963448192823/
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018
HELPFUL LINK http://www.technologystudent.com/despro_ﬂsh/iterative1.html

## Slide 10
USING PHOTOGRAPHIC / VIDEO EVIDENCE
www.technologystudent.com © 2018 V.Ryan © 2018
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
https://www.facebook.com/groups/254963448192823/
RECORDING FEEDBACK
USING FEEDBACK TO DEVELOP A DESIGN
CRITICAL ANALYSIS
RELEVANT RESEARCH SKILLS
HERE ARE SOME DESIGN TOOLS
CUSTOMER PROFILING WRITING A PROBLEM AND BRIEF WRITING A SPECIFICATION
SKETCHING
CAD 3D DESIGN
COMPOSING AN INSPIRATIONAL MOODBOARD
MODEL MAKING
QUESTIONNAIRES / SURVEYS
WORKING DRAWINGS etc...
PLANNING SKILLS
MATERIALS TESTING
PRODUCT TESTING
MATERIAL SELECTION
COLLECTING ANTHROPOMETRIC DATA LEADING TO AN ERGONOMIC DESIGN
HEALTH AND SAFETY
EVALUATIVE SKILLS
MARKETING
MANUFACTURING PROCESSES
THERE ARE MANY MORE DESIGN TOOLS - CAN YOU NAME SOME?
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018
INCLUSIVITY

## Slide 11
www.technologystudent.com © 2018
https://www.facebook.com/groups/254963448192823/
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
V.Ryan © 2018
CAREFULLY STUDY THE SAMPLE ITERATIVE DESIGN SHEET ON THE NEXT SLIDE. YOUR TEACHER MAY HAVE A PRINTED VERSION FOR YOU TO STUDY.
WHAT DESIGN TOOLS / TECHNIQUES DO YOU SEE BEING USED ON THIS SINGLE PAGE?
YOU SHOULD FIND, A VARIETY OF DESIGN TOOLS / TECHNIQUES HAVE BEEN UTILISED.
THIS IS A TYPICAL EXAMPLE OF THE ITERATIVE DESIGN ASPECT OF THE NEA.
STUDENT EXERCISE
HELPFUL LINK http://www.technologystudent.com/despro_ﬂsh/iterative1.html

## Slide 12: MEMPHIS STYLE MP3 PLAYER - SAMPLE ITERATIVE DESIGN SHEET
This is my ﬁrst basic idea for an MP3 player. It is composed of three main parts, two speakers and a docking station.
SPEAKER
MP3 STATION
The ‘back’ view shows the interlocking speaker and MP3 station system.
The design is based on the Memphis Design Movement. The speakers are rectangles / squares and they could be diﬀerent sizes and colours, producing an unusual design.
SPEAKER
The system has a built in transformer, which means it can be plugged into a mains supply (240 volts). Batteries ﬁt into either base unit, providing power when playing the system outside.
SPEAKERS - DISTANCE EXTENDED
6 AA batteries are needed for use away from mains electricity.
Each speaker arm, can be altered to any angle between 0 to 90 degrees. I tested this aspect with the model. This means that the sound can be directed in almost any direction, ideal for a party. If two people are sat at diﬀerent sides of a room, the speakers can be independently angles for perfect listening.
The MP3 station has two headphone sockets. This allows two people to listen to the same music, without disturbing other people in the room.
The MP3 system is stable and very unlikely to be knocked over. It will be designed to conform to British and European safety standards.
SPEAKER ARMS
The card model proved to be useful. It allow me to see the product in 3D and to handle it. It was useful with my focus group
The distance of each speaker from the docking station, can be altered independently of each other.
My client liked this idea although he suggested that it may be possible to trap ﬁngers when shortening the distance between the speakers
My client suggested adding artistic detail to the back of the speakers, improving the aesthetics.
My client suggested making it possible to angle the speakers, so that the sound could be focussed on any point in the room.
Internet Research size of AA batteries
My focus group of potential clients like this concept. However, they suggested that the mp3 player could be manufactured in a number of styles, whilst at the same time keeping the same shape / form. This would give the product a wider appeal.
player can be controlled by a range of smart phones through a freely available app. It has its own control pad, in a range of sizes of button sizes. It also has voice control. Ideal or people who are short sighted or have arthritic hands/ﬁngers.
The anthropometric data collected on hand sizes, has been applied to the mp3 player, so that it is easy to adjust.
D
E
This is the ﬁnal ‘concept’ design. It clearly shows the Memphis inﬂuence. It is colourful, unusual and the speakers are diﬀerent sizes, although they deliver equal sound volumes.
My research shows that high density polystyrene is the best choice for the casing, due to it’s physical
Focus group suggestion - INCLUSIVITY - the mp3 properties. Injection moulding being
the manufacturing process.

## Slide 13
CLICK ON THE LINK BELOW FOR A THREE MINUTE VIDEO THAT EXPLAINS ITERATIVE DESIGN
https://www.youtube.com/watch?v=eWcFFmtlBt4
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018
www.technologystudent.com © 2018
https://www.facebook.com/groups/254963448192823/
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
V.Ryan © 2018

## Slide 14: COMPLETE ITERATIVE DESIGN CYCLE
1. DESIGN CONCEPT
2. INITIAL LARGE NUMBER OF SKETCHES / IDEAS
4. INITIAL MODELS
3. CAD
7. INITIAL TESTING AND FEEDBACK
6. CHECK IDEAS AGAINST
THE SPECIFICATION
3. MATERIALS TESTING
1. IMPROVEMENTS TO SELECTED DESIGNS
5. TESTING OF 3D PROTOTYPES
7. INITIAL EVALUATION / CONCLUSIONS
6. CLIENT / TARGET MARKET
INPUT / FEED BACK
2. FOCUSSED ANTHROPOMETRIC
RESEARCH, LEADING TO ERGONOMIC DESIGNS
= EXPLORE = CREATE = EVALUATE
1. ONE IDEA TO BE FULLY DEVELOPED.
2. FINAL DRAWINGS
3. FINAL PROTOTYPE MANUFACTURED
4. FULL TESTING BY FOCUS GROUP AND CLIENT
5. FINAL EVALUATION AGAINST SPECIFICATION
6. FINAL IMPROVEMENTS AND MODIFICATIONS
1. DESIGN PROBLEM IDENTIFIED
3. ESTABLISH A TARGET MARKET TYPICAL CUSTOMER
AND STAKE HOLDERS
4. FORMULATE A DESIGN BRIEF
5. FOCUSSED ANALYTICAL
RESEARCH OF
EXISTING PRODUCTS
7. JUSTIFIED SPECIFICATION
6. INSPIRATIONAL MOODBOARD
2. PROVE A PROBLEM EXISTS
1
2
4
3
THE DESIGNER
5. ENVIRONMENT / SUSTAINABILITY
4. ENVIRONMENT / SUSTAINABILITY
HELPFUL LINK http://www.technologystudent.com/despro_ﬂsh/iterative1.html
www.technologystudent.com © 2018
https://www.facebook.com/groups/254963448192823/
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
V.Ryan © 2018

## Slide 15: HOW ITERATIVE DESIGN WORKS
Example 1: If a student understands the purpose of a questionnaire / survey and how to conduct one, he/she will be able to decide when to use this tool when desiging (and how many times). This applies to each ‘design tool’, including CAD, thumbnail sketching and model making.
Each design tool can be utilised many times, during the iterative design process.
Example 2: The ‘design tool’ called ‘feedback’. If a student knows how to record feedback, what to ask potential customers and stakeholders and how to turn the gained knowledge into an improved design, this skill can be used regularly, during the iterative design process.
There is no set way of designing. The student has freedom to use the ‘design tools’ at his/her disposal at any time, whilst designing at product.
https://www.facebook.com/groups/254963448192823/
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
www.technologystudent.com © 2018 V.Ryan © 2018
HELPFUL LINK http://www.technologystudent.com/despro_ﬂsh/iterative1.html

## Slide 16: HOW MANY PAGES FOR EACH CYCLE OF ITERATIVE DESIGN?
HELPFUL LINK http://www.technologystudent.com/despro_ﬂsh/iterative1.html
CYCLE ONE - 5 to 8 SHEETS
CYCLE TWO - 5 to 8 SHEETS CYCLE THREE AND FOUR - 10 SHEETS
HOWEVER - THE TOTAL NUMBER OF DESIGN SHEETS FOR THE ENTIRE PORTFOLIO SHOULD BE APPROXIMATELY 20
The number of design sheets in each ‘cycle’ of the iterative process will vary. This will depend on the approach taken by the student and the context / design problem he/she is working on. Some students will produce more initial designs (cycle two), whilst other students will spend longer on the development of ideas and consequently produce more design sheets for cycle three. This is due to the ﬂexibility of the iterative design process.

## Slide 17: CYCLE 1
IDENTIFYING & INVESTIGATING DESIGN POSSIBILITIES
1. DESIGN PROBLEM IDENTIFIED
www.technologystudent.com © 2018 V.Ryan © 2018
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
https://www.facebook.com/groups/254963448192823/
3. ESTABLISH A TARGET MARKET TYPICAL CUSTOMER
AND STAKE HOLDERS
5. ANALYTICAL RESEARCH
OF
EXISTING PRODUCTS
4. FORMULATE A DESIGN BRIEF
7. JUSTIFIED SPECIFICATION
6. INSPIRATIONAL MOODBOARD
2. PROVE A PROBLEM EXISTS
1
HELPFUL LINK http://www.technologystudent.com/despro_ﬂsh/iterative2.html

## Slide 18
CYCLE ONE COVERS THE EXAMINATION BOARDS ‘OBJECTIVES’ OUTLINED BELOW
AQA
AO1: Identify, investigate and outline design possibilities to address needs and wants.
A03: Analyse & evaluate
OCR
Explore (AO1)
Identifying requirements
Learning from existing products and practice
EDEXCEL
Component 2
  1.1 Investigation of needs and research
  1.2 Product Speciﬁcation including a Design Brief
www.technologystudent.com © 2018 V.Ryan © 2018
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
https://www.facebook.com/groups/254963448192823/

## Slide 19: WHAT SHOULD BE INCLUDED IN THIS ‘CYCLE’?
Begin by investigating the selected CONTEXT to identify design possibilities / design problems. Consider these in-depth.
A client / potential customer is identiﬁed, as well as a suitable justiﬁed design problem, that will be solved through the portfolio.
The needs and design requirements of the client / potential customer are deﬁned, after a enquiry and analytical research
The inspirational work of designers and design movements are considered.
Produce a Design Brief and Justiﬁed Speciﬁcation.
www.technologystudent.com © 2018 V.Ryan © 2018
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
https://www.facebook.com/groups/254963448192823/
HELPFUL LINK http://www.technologystudent.com/despro_ﬂsh/iterative2.html

## Slide 20
THE NEXT TWO SLIDES SHOW ONE WAY OF INVESTIGATING A CONTEXTUAL CHALLENGE.
SAMPLE CONTEXT - “WORKING COMFORTABLY WITHOUT A DESK OR TABLE”
www.technologystudent.com © 2018 V.Ryan © 2018
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
https://www.facebook.com/groups/254963448192823/
HELPFUL LINK http://www.technologystudent.com/despro_ﬂsh/iterative2.html
EXERCISE - IDENTIFYING A GENUINE DESIGN PROBLEM
THE LINK BELOW WILL TAKE YOU TO A NUMBER OF PROBLEM / DESIGN CARDS. THEY SHOW HOW A PROBLEM CAN BE IDENTIFIED AND A SIMPLE DESIGN BRIEF WRITTEN.
http://www.technologystudent.com/despro_ﬂsh/new_prob1.html
www.technologystudent.com © 2018
https://www.facebook.com/groups/254963448192823/
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
V.Ryan © 2018

## Slide 21: IDENTIFYING & INVESTIGATING DESIGN POSSIBILITIES STARTING WITH A CONTEXT
SAMPLE CONTEXT - WORKING COMFORTABLY WITHOUT A DESK OR TABLE
Design possibilities identiﬁed and thoroughly explored. |  |  | 
In this example, the main theme(context) has been written in the centre of the page. Various design opportunities have been |  |  | 
written around the page. The ‘BLACK’ ink highlights a possible area for further investigation. The ‘RED’ writing indicates a potential problem(s) to solve. |  |  | 
HELPFUL LINKS
http://www.technologystudent.com/despro_ﬂsh/new_prob1.html
www.technologystudent.com © 2018 V.Ryan © 2018
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
https://www.facebook.com/groups/254963448192823/
http://www.technologystudent.com/pdf14/POSTER_FIND_PROBLEM1.pdf
There are many ways of analysing a contextual challenge. Below is just one example. Quite simply write the context in the centre of a design sheet and identify design opportunities.

## Slide 22: ANALYSING THE CONTEXTUAL CHALLENGE STUDENTS WILL IDENTIFY DESIGN POSSIBILITIES
“WORKING COMFORTABLY WITHOUT
A DESK OR TABLE”
WHEN SEATED
Many students do not work at a table or even have access to a table.
Design an accessory, that enables a student to work comfrotably, when sat in a chair / on a seat.
WHEN USING PUBLIC TRANSPORT
Students often work on the move. Mobile phones and tablets are an excellent example of devices being used. Design opportunity - being distracted, not focussed, potential accidents, dropping the device.
WHEN STANDING / WALKING
ANTHROPOMETRICS AND ERGONOMICS
Products should be designed to ﬁt the user. Collect anthropometric data and apply the ﬁndings to an ergonomically designed product, such as a device holder, stationery rest or accessory, to enable working without a table.
SECURITY
Security when using electronic devices such as tablets, is an issue. When in public, a person using a device can be the focus of people with criminal intent.
Designing a solution that makes the use of electronic devices safe and secure.
HEALTH AND SAFETY
This is closely linked to ergonomics.
Repetitive strain injuries can develop when using equipment and electronic devices over time.
Design a device or accessory, that reduces the risk of this type of debilitation injury.
STORAGE
Students use a range of equipment when working sat in an ‘easy’ chair.
Design a storage unit / rack, that will allow easy access to stationery equipment, when stretching, sat in a chair etc.......
ACCESSORIES AND INCLUSIVITY
Educational equipment should be designed to ensure inclusive use, in terms of age group, gender, disabilities, intellectual capacity.
Design a device or an accessory that supports learning and allows use by the widest possible range of people.
BRITISH AND EUROPEAN STANDARDS
European and British Standards aim to sure that products are safe to use. This often relates to comfort and reducing the risk of injury, for example, in the case of furniture design.
Design an educational aid or an accessory that relates to working without a table, and complies with both sets of legislation.
TESTING RIGS
Testing rigs are often constructed to put products under ‘stress tests’.
Design a test rig, that is capable of checking the durability and comfort of a device used to aid learning, when sat in a chair.
INSTRUCTION BOOKLET
Educational / electronic devices can be diﬃcult to use, as instructions are often in electronic form. Design an instruction booklet, that can be easily stored and contains all the information to ensure safe and proper use of the device. It should be easy to read, well illustrated and packaged.
SHOP DISPLAY
The employees of retailers, regularly retrieve and return educational accessories to shop shelves, throughout the working day.
Design a system to enable the safe and easy removal and return of educational accessories, to and from shop shelves.
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 23
THIS IS AN ALTERNATIVE LAYOUT TO THE SHEET

## Slide 24
THE NEXT TWO SLIDES EXPLAIN A WAY OF CLEARLY IDENTIFYING THE DESIGN PROBLEM, THAT HAS BEEN SELECTED BY INVESTIGATING THE CONTEXTUAL CHALLENGE - AS SEEN IN THE TWO PREVIOUS SLIDES .
SAMPLE CONTEXTUAL CHALLENGE - “WORKING COMFORTABLY WITHOUT A DESK OR TABLE”
www.technologystudent.com © 2018 V.Ryan © 2018
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
https://www.facebook.com/groups/254963448192823/
https://www.facebook.com/groups/254963448192823/
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
www.technologystudent.com © 2018 V.Ryan © 2018
HELPFUL LINK http://www.technologystudent.com/despro_ﬂsh/new_prob1.html

## Slide 25: CLEAR IDENTIFICATION OF THE DESIGN OPPORTUNITY
This sheet clearly identiﬁes the selected design opportunity.
Potential clients are referenced.
Evidence that the problem is a genuine problem worth solving, is achieved through a questionnaire. A justiﬁed need.
This is an example of a design sheet that refers to the selected design opportunity. It clearly identiﬁes the speciﬁc design problem, stemming from the contextual sheet.
HELPFUL LINK http://www.technologystudent.com/despro_ﬂsh/new_problem1.html
www.technologystudent.com © 2018 V.Ryan © 2018
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
https://www.facebook.com/groups/254963448192823/
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 26
Objective 1: Identiﬁcation of a Need or Opportunity Leading to a Design Brief
I carried out a survey of fellow pupils and teaching staﬀ, to identify the percentage who regularly complete written work by resting their work on their knees / lap. Also, if there is a genuine demand for a ‘device’ / writing aid, which allows the user to work comfortably, whilst supporting work in this way.
1. 50 Year 11 pupils and 50 teachers were asked, ‘do you regularly rest work on your knees / lap, whilst completing it?’ 78 % said yes.
Working with a board resting on a knee or lap, is not the most comfortable position. It eventually causes neck and back ache and results in a lack of concentration and focus. This inevitably aﬀects the quality of work.
PROOF / EVIDENCE
2. 50 Year 11 pupils and 50 teachers were asked, ‘have you ever suﬀered from neck / back ache when, resting work on your knee / lap?’ 55% said yes.
2. 50 Year 11 pupils and 50 teachers were asked, ‘would you purchase a reasonably priced product, that solved the design problem?’ 65% said yes.
78% 55% 65%
www.technologystudent.com © 2018 V.Ryan © 2018
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
https://www.facebook.com/groups/254963448192823/
THE PROBLEM / SITUATION / IDENTIFICATION OF NEED
THE PROBLEM
Most of my friends complete their home work, sat on a chair or settee, in front of the TV. Or they work in their bedroom, sat on an ‘easy’ chair. They rest their paper on a board, which rests on their knee / lap. The problem is that it is diﬃcult to support paper and consequently to write neatly, even if work is supported on your knee. Oﬃce workers who take work home, also have this problem, when working in a more relaxed way, such as this.
Lighting is also a problem. The light source never seems to be in the right position for work and a shadow is cast preventing work being seen properly. This is irritating and probably harmful to eyesight, if working for sometime.
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/ www.technologystudent.com © 2018
V.Ryan © 2018

## Slide 27
THE NEXT TWO SLIDES SHOW AN EXAMPLE OF IDENTIFIYING A SPECIFIC CLIENT, PRESENTING THE CLIENT NEEDS / REQUIREMENTS AND A DESIGN BRIEF.
SAMPLE CONTEXTUAL CHALLENGE - “WORKING COMFORTABLY WITHOUT A DESK OR TABLE”
www.technologystudent.com © 2018 V.Ryan © 2018
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
https://www.facebook.com/groups/254963448192823/
https://www.facebook.com/groups/254963448192823/
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 28
INVESTIGATE CLIENT NEEDS AND WANTS AND FACTORS INCLUDING ECONOMIC AND SOCIAL CHALLENGES
This design sheet clearly identiﬁes the client / user. A potential wider range of users have also been identiﬁed.
Needs and wants of the client are discussed and justiﬁed.
Design Brief which clearly justiﬁes how they have considered their user/client's needs and wants and links directly to the context selected
A user/client has been clearly identiﬁed. The student has undertaken a comprehensive investigation of their needs and wants, with a clear explanation and justiﬁcation.
HELPFUL LINK
http://www.technologystudent.com/despro_ﬂsh/cus1.html
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 29
TYPICAL CUSTOMER / POTENTIAL USER PROFILE SHEET
Below is a description of a specific client. He has
commissioned the design and manufacture a prototype of my product.
SPECIFIC CLIENT
CLIENTS DESIRED PRODUCT OUTCOME
‘I would like a lightweight device that allows me to write neatly and yet allows me to sit in a comfortable easy chair. In addition, I need an adjustable light source, so that I can focus the light where I need it.’
Jeff Smith
POTENTIAL RANGE OF CUSTOMERS
BACKGROUND
Oﬃce manager for a local college. Needs to work at home and prefers to work sat on an easy chair, with the work supported on his lap.
Also works at a desk, when at his workplace.
DESIGN REQUIREMENTS
Client view and opinion:
‘I need a device or system that enables me to work in a more comfortable seating position. I do not want or need to work at a desk all the time. I like to be sat with the rest of the family, when I am reading through reports or writing memos and letters. There are even times at work, when I am in a meeting and I need to take notes, when sat on an ordinary chair. I do not need to work always at a table, in an oﬃce. However, resting work on a board on my lap, leads to back and neck ache.’
EXERCISE BOOKS
CLIPBOARDS
EXCERISE PAPER
ART SKETCH BOOK
READING BOOK
Pupils / students - working on homework.
Oﬃce workers and Clerical workers - paper work taken home for completion.
Anyone - who prefers to be sat in a relaxing position, whilst reading.
These are examples of the type of products that people hold / use when working and reading at home. If these are used whist sat in an easy chair, back and neck ache can result.
Pupil quote: ‘I gets lots of home work and like working in front of the ﬁre, not at a desk’.
Clerical worker quote: ‘I take too much work home and like working whilst sat on an easy chair. I work at a desk, all day long ’.
Parent quote: ‘I like reading and writing letters when sat on a comfortable chair and in the same room as my children’.
I am going to design a suitable ‘stationery rest’, for use when sat on an easy chair or settee, when sketching, writing and reading. It will have an adjustable light source, to illuminate the paperwork on the rest. It will be easy and comfortable to use . The innovative stationery rest will help prevent back and neck ache.
It will be suitable for a range of users and a broad age range, making writing, reading and sketching away from a table, a pleasure.
https://www.facebook.com/groups/254963448192823/
DESIGN BRIEF
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
www.technologystudent.com © 2018 V.Ryan © 2018
https://www.facebook.com/groups/254963448192823/
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 30
THE NEXT SET OF SLIDES SHOW THE PRESENTATION OF ANALYTICAL RESEARCH.
1. EXISTING DESIGNS TO AID FUTURE PRODUCT DESIGN
2. QUESTIONNAIRE TO INFORM FUTURE DESIGNING
3. ANALYTICAL MOOD BOARD
4. ANALYTICAL RESEARCH SPECIFIC TO THE CLIENT
5. JUSTIFIED SPECIFICATION.
DESIGN BRIEF - ‘stationery / writing rest’, for use when sat on an easy chair or settee, when sketching, writing and reading.
www.technologystudent.com © 2018 V.Ryan © 2018
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
https://www.facebook.com/groups/254963448192823/
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 31: ANALYTICAL RESEARCH OF EXISTING PRODUCTS
When researching existing products, it is important to focus on those that may contribute in some way, to a new or improved design.
Existing or similar products, may have functions and features you ﬁnd of interest or partly solve the design problem you are working on. Carefully analysing your research ﬁndings, could help you design a successful, innovative product.
If you identify an interesting function or feature, the next stage is to determine why the function / feature has been included.
www.technologystudent.com © 2018 V.Ryan © 2018
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
https://www.facebook.com/groups/254963448192823/
HELPFUL LINK http://www.technologystudent.com/despro_ﬂsh/focusres1.html

## Slide 32: RESEARCH AND ANALYSIS OF EXISTING PRODUCTS
What materials have been used in its Is the cost of the product a
Is the size, weight and shape important?
Summary of conclusions:
It must be possible for right and left handed people to use my product, with equal comfort.
It must be ﬁrm and not move at all, when being used. A good writing
position is vital.
Plywood could be the ideal material for the writing / sketching surface. The cost must be relatively low. This deﬁnitely helps the sales of the device seen above.
construction and why?
The stationery rest is manufactured from plywood. This is ideal as it does not warp or twist out of shape. It provides a ﬁrm surface for writing and sketching.
The product is lightweight and
easy to ﬁt and take oﬀ the chair.
The shape allows the arm of the
user to rest comfortably,
providing a good writing position.
http://www.alibaba.com/product-detail/wood- school-chair-with-writing- board_1130856362.html
factor in its success?
Both the chair and the stationery rest cost £18.00. This is an extremely good price and is one reason for its success.
What are the interesting features?
This Lap Rest is a simple idea. The main feature of interest is that the stand rests between the users legs, keeping it stable. This could be used even when sat on an easy chair. The basic structure makes it easy to manufacture. However, would it be uncomfortable to keep under your legs? for a sustained amount of time.
Summary of conclusions:
I must keep my design simple, so that it is easy to use and manufacture. Although the rest above is set at one angle, I may design one that can be altered. My product must to lightweight, possibly manufactured from polypropylene. The product will be easy to clean, if polypropylene is used.
Injection moulding is an ideal process, for manufacturing a one piece product.
If injection moulding is the selected manufacturing process, large numbers of the product should be made, to keep costs as low as possible.
An adjustable product is needed so that the product has a large range of potential
customers.
UNCOMFORTABLE?
What are the interesting functions?
The rest is set at one angle and can be used for resting paper, a magazine or book and even a laptop.
What does the customer / target market ﬁnd interesting about the product.
My speciﬁc client said that this product looked quite good, although he suggested that it may be uncomfortable to use for a prolonged time.
Is the size, weight and shape important?
The size and weight are ideal, as it could be stored easily when not in use.
What materials have been used in its construction and why?
Polypropylene is a good choice because it is lightweight and can be moulded to form a complex shape.
Is the cost of the product a factor in its success?
The product costs £22, which reﬂects the cost of injection moulding small numbers.
https://www.facebook.com/groups/254963448192823/
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
What are the interesting features?
The interesting feature of this ‘stationery rest’ is that it ﬁts ﬁrmly on to the chair and does not ‘wobble’ or move, when in use. It is also slightly at the side of the chair allowing comfortable use. However, one big negative is that it is for right handed people. A second left handed version would have to be bought. This is another negative.
What are the interesting functions?
Allows writing in a formal setting as this chair would normally be seen in a classroom.
What does the target market
ﬁnd interesting about the product.
My potential customers do not like the stationery rest, as it is not for an easy chair. However, in a formal setting of a classroom it is ideal.
www.technologystudent.com © 2018 V.Ryan © 2018
https://www.facebook.com/groups/254963448192823/
The product must be lightweight and easy to move.
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 33: RESEARCH AND ANALYSIS OF EXISTING PRODUCTS
What materials have been used in its Is the cost of the product a factor in its
Summary of conclusions:
An adjustable frame, could allow for a large range of potential users, of diﬀerent ages. Lightweight aluminium will be considered for my product, if I design a frame based system.
Aluminium is recyclable and this product can be dismantled easily, making it
environmentally friendly. A sustainable product.
I will keep the costs down, as a very expensive product, may price itself out of the market and not be bought in quantities.
ADJUSTABLE LAP REST
What are the interesting features?
This adjustable ‘rest’ has some very interesting features. It is fully adjustable, ensuring the comfort of the user.
One limiting feature, is that the frame may restrict arm and elbow movement, in certain
circumstances.
It does not interfere with leg movement, although it may be a little diﬃcult to move, due again to the frame.
What are the interesting functions?
The range of adjustment, which allows the user to work when lying or sat down. Also, the fact that it can be folded away unlike many other frame based writing rests. Storage when the product is not in use is another interesting function. This product will ‘ﬁt’ around most people as it ergonomically designed.
What does the target market
ﬁnd interesting about the product.
My client quite liked this design. He said, ‘I like the adjustability especially the height adjustment. This feature could be useful’.
The product is environmentally friendly as the materials can be recycled.
Is the size, weight and shape important?
The aluminium frame is light, although the use of aluminium and associated engineering, increases the overall cost of manufacture. The shape is very interesting, as it changes shape when put into diﬀerent conﬁgurations.
construction and why?
Lightweight aluminium tube is used in the products construction.
Aluminium can be recycled as well,
making the product sustainable
success?
The cost of this product is a negative, as it is very expensive at £82.00. There are many cheaper products on the market, although in most cases they are not adjustable.
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018
www.technologystudent.com © 2018
https://www.facebook.com/groups/254963448192823/
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
V.Ryan © 2018

## Slide 34
ANALYTICAL RESEARCH OF POTENTIAL CUSTOMERS
Questionnaires are a very useful research 'tool'. If the right questions are asked, the ﬁndings can help guide the development of a product.
The key is to ask the right focussed questions and to analyse the ﬁndings carefully.
The questions should be targeted and direct, not general. Only ask relevant questions.
For example, asking potential customers of a house alarm system, 'how many zones (rooms) must the alarm cover protect?' is a direct and necessary question. It will help you to determine how many inputs (sensors) the alarm circuit requires. However, asking potential customers, 'do you want the alarm to be loud?', is far too generalised and will not return important research ﬁndings.
Asking questions that help you determine the needs or requirements of the customer, also helps the designer to focus on important research information.
HELPFUL LINK http://www.technologystudent.com/despro_ﬂsh/focussedq1.html
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 35: ANALYTICAL RESEARCH OF POTENTIAL CUSTOMERS
A B C D
QUESTIONNAIRE
1. Would a writing rest be of use to you at home?
2. Would a writing rest be of use to you at work?
3. Which one of the writing rests shown below, has the most features / functions that you require?
6. Which Art Movement is your favourite?
MEMPHIS ART DECO
BAUHAUS
POP ART
YES
NO
YES NO
A
4. With reference to your selected product from question 3, describe the features / functions you ﬁnd the most interesting?
I like writing rest ‘A’ because: It has an LED light that can be focussed directly where the user wants it. The rest has a picture and there is a selection to choose from. The rest has a groove for a pen , so that it does n roll away
5. What would you be prepared to pay for a quality writing rest? Select one from the range below. Tick your choice.
£5 - £10 £10 - £15 £15 - £20 £20 - £25
85%
22%
0% 50% 100%
4. With reference to your selected product from question 3, describe the features / functions you ﬁnd the most interesting?
Most popular features and functions:
LED Light
Groove for pen
Would a writing rest be of use to you at home?
Would a writing rest be of use to you at work?
Which one of the writing rests shown below, has the most features / functions that you require?
49%
22%
100%
0%
50%
A B C D
12%
17%
62%
Image / pictures
9%
29%
The information I gain from my questionnaire will help me design my writing rest.
SAMPLE QUESTIONNAIRE
REASONING BEHIND THE QUESTIONS
This is a copy of the questionnaire I gave to ﬁfty people. I wanted to ﬁnd out speciﬁc information:
Questions 1 and 2 will help determine if my product is likely to be used at home and/or work.
Questions 3 and 4 identiﬁes the most popular features according to potential customers.
Question 5 will provide information about the most popular price range, genuine potential customers are prepared to pay.
Question 6 is about the style of writing rest that customers may want to purchase.
CONCLUSIONS / SUMMARY OF RESULTS
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 36
A mood board can be extremely useful as a research tool, especially when working closely with a client / potential customer. For example, ‘my’ client wants me to design a writing rest for an easy chair. When talking to him in order to determine the overall style of the design, it is obvious that he has an interest in art movements such as; Art Deco and Bauhaus. By building up a 'reasoned' mood board on these art movements, I will be able question my client as to which style or features he would like to be applied to the writing rest.
The mood board will not only be composed of pictures but also text that explains the reason for including the pictures. The text will also explain which art movement features, are of interest and may be applied to the design.
www.technologystudent.com © 2018 V.Ryan © 2018
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
https://www.facebook.com/groups/254963448192823/
ANALYTICAL RESEARCH - MOOD BOARD
HELPFUL LINK http://www.technologystudent.com/despro_ﬂsh/anmood1.html
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 37: ANALYTICAL RESEARCH – MOOD BOARD
BAUHAUS
www.technologystudent.com © 2018 V.Ryan © 2018
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
https://www.facebook.com/groups/254963448192823/
When talking to my client in order to determine the overall style of the design, it became obvious that he has an interest in Art Movements such as; Art Deco and Bauhaus. By building up a reasoned mood board on these art movements, I will be able question my client, as to which style or features he would like to be applied to the writing rest. The mood board will be a very useful research tool.
ART DECO
The buildings have features such as symmetry, curves and shapes that could transfer to a writing rest. The patterns and shapes could be applied to decorate the ﬁnal product. Further to this, the style of the furniture and the materials used, could inﬂuence my design.
These buildings reﬂect perfect symmetry that could be applied to my product. I like the chrome eﬀect of the Empire State Building.
These geometrical shapes are typical Art Deco. I like the colours and shapes, as they could provide my product with an authentic style.
The corners and straight patterns could be used on the writing surface.
My product could be manufactured from these materials. I like the veneered surface on the table. The use of chromed steel on the chairs is eﬀective.
Bauhaus is a modernist style, that could be applied to my innovative product. In its day, Bauhaus design was new and refreshing. This design movement experimented with new materials, which could be what I need to do when designing my product.
Bauhaus shapes and patterns are attractive and are still regarded as modern and up to date.
My client has pictures like these on his oﬃce walls.
I like the unusual style and especially the handles on these kettles. Handles may be needed on my writing rest.
I need a light source on my writing rest. The ﬂexible stem on the ﬁrst light and the way it is clamped to the surface, could be what I need for my product. The focussed light of the second stand could work on my product. Both lights are stylish and modern.
The shape of the frame of these pieces of Bauhaus furniture could inﬂuence my design.
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/ www.technologystudent.com © 2018 V.Ryan © 2018
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 38
Ergonomic research can sometimes be quite generalised.
However, in order to limit the amount of research carried out and to eliminate irrelevant research, there is another approach. The ergonomic research in the following example, is focussed on the client and acquiring only essential anthropometric data.
The next example, shows anthropometric data being collected for the design of a 'writing rest' for an easy chair. This is called Primary Research, as it involves the designer / researcher carrying out his / her own research and not taking existing research from books or the internet.
www.technologystudent.com © 2018 V.Ryan © 2018
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
https://www.facebook.com/groups/254963448192823/
ANALYTICAL RESEARCH OF POTENTIAL CUSTOMERS
HELPFUL LINK http://www.technologystudent.com/despro_ﬂsh/ergorest1.html
https://www.facebook.com/groups/254963448192823/
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 39: ANALYTICAL RESEARCH OF POTENTIAL CUSTOMERS
B
ERGONOMICS PRIMARY RESEARCH
I collected primary research for three important measurements, relating to my product.
Average comfortable reach length (A): I need this data so that the writing rest I design is not to large. The rest must ﬁt within the arm reach of most people.
Average seating height (B): I need this measurement because this distance may inﬂuence the design of the writing rest, especially if the rest attaches to a chair.
Average body width (C): I need this measurement, so that I ensure that the rest is a suitable width for the largest range of users.
Average hand width (D) and length (E): I need these measurements because they will help me work out the size of the writing rest and how it can be handled.
PUPIL/PERSON | A | B | C
Person A | 600mm | 450mm | 500mm
Person B | 534mm | 436mm | 522mm
Person C | 589mm | 425mm | 515mm
Person D | 590mm | 395mm | 506mm
Person E | 610mm | 412mm | 545mm
Person F | 500mm | 423mm | 534mm
Person G | 615mm | 428mm | 535mm
Person H | 602mm | 422mm | 560mm
Person I | 590mm | 480mm | 545mm
Person J | 595mm | 435mm | 577mm
Person K | 605mm | 456mm | 561mm
Person L | 625mm | 400mm | 400mm
TOTAL(S) | 7055mm | 5162mm | 6300mm
AVERAGE | 588mm | 430mm | 525mm
D
E
PUPIL/PERSON | D | E
Person A | 155mm | 82mm
Person B | 149mm | 59mm
Person C | 152mm | 52mm
Person D | 145mm | 70mm
Person E | 139mm | 75mm
Person F | 135mm | 76mm
Person G | 142mm | 81mm
Person H | 147mm | 78mm
Person I | 152mm | 70mm
Person J | 148mm | 72mm
Person K | 153mm | 81mm
Person L | 135mm | 76mm
TOTAL(S) | 1752mm | 872mm
AVERAGE | 146mm | 72.6mm
Typical easy chair used by my speciﬁc client. The type of chair the writing rest will be designed to ﬁt. Ergonomic data will be required so that the rest can be successfully designed.
84cm
74cm
90cm
www.technologystudent.com © 2018 V.Ryan © 2018
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
https://www.facebook.com/groups/254963448192823/
41cm
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
A C
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 40: THE JUSTIFIED SPECIFICATION
www.technologystudent.com © 2018 V.Ryan © 2018
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
https://www.facebook.com/groups/254963448192823/
HELPFUL LINK http://www.technologystudent.com/designpro/newspec1.html
A ‘speciﬁcation’ is a summary of the key points, identiﬁed by your research and analysis. Your research should be in detail. Now is the time to draw all the research / evidence together, in a clear speciﬁcation. The speciﬁcation can be a list of key points / sentences, that help to determine the future design and development of the product.
When writing a speciﬁcation, refer where possible, to the research you have carried out. You could refer to speciﬁc research pages such as, the problem / brief page, the existing products pages, ergonomics and questionnaire pages. You should consider including 'quotes' from your potential customers and / or referring to page numbers. Usually, each speciﬁcation point is justiﬁed by referring to aspects of your research or the design requirements.
One way of setting out a 'justiﬁed' speciﬁcation is shown next. In the ﬁrst column a speciﬁcation point is written as a sentence(s). In the second column, the point is justiﬁed by referring back to speciﬁc research ﬁndings. Further justiﬁcation for each speciﬁcation point, can be added in a third column. The third column, makes reference to how each speciﬁcation point will inform future design developments.

## Slide 41: HELPFUL LINK http://www.technologystudent.com/designpro/newspec1.html
COMPREHENSIVE DESIGN SPECIFICATION
JUSTIFICATION LINKING TO THE NEEDS AND WANTS OF THE CLIENT/USER
FULLY INFORMS SUBSEQUENT DESIGN STAGES
www.technologystudent.com © 2018 V.Ryan © 2018
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
https://www.facebook.com/groups/254963448192823/

## Slide 42
My Product Specification is written below. It is a check list that will help me develop my product.
It has been checked and agreed with my client / customer
www.technologystudent.com © 2018 V.Ryan © 2018
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
https://www.facebook.com/groups/254963448192823/
MY SPECIFICATION
PRODUCT: EASY CHAIR WRITING REST
EVIDENCE FROM RESEARCH - JUSTIFICATION
MY SIGNATURE:
CLIENT SIGNATURE:
FURTHER JUSTIFICATION
SPECIFICATION POINT
POTENTIAL CUSTOMERS: The ‘writing rest’ must be useful and appeal to a wide range of potential customers.
This is shown by my initial research (page/slide 1), when investigating the design problem and brief. The questionnaire shows that both pupils and teachers are interested in this product.
Furthermore, if I design a writing rest that appeals to a wide age range, it is more likely to sell successfully, in large numbers.
FUNCTIONS - EASE OF USE: The
‘writing rest’ must allow the user to write and read comfortably, whilst sat in an easy chair.
A majority of people I asked about reading and writing whilst sat in an easy chair, said that this was diﬃcult and often uncomfortable (see design problem / brief and potential customer sheets).
An easy to use reading / writing rest could solve this problem.
Many of my friends have said that the writing rest must be easy and comfortable to use. This is a priority.
FUNCTIONS - LIGHTING: The ‘writing rest’ should have an integrated light source.
When questioning people about the design problem, many said that the light source was essential. A quote from the detailed questionnaire says about an existing product, ‘It has an LED light that can be focussed directly where the user wants it’.
When reading or writing whilst sat on a easy chair, the room light source often casts a shadow. This makes reading diﬃcult and sometimes unpleasant.
LIGHTWEIGHT: The writing rest should be lightweight.
My research into existing/similar products, suggests that a successful writing rest must be lightweight (see existing products section of my research).
A light weight writing rest will be comfortable on the knees and be easy to carry around and store, when it is not in use.
ADJUSTABLE: The writing rest should be adjustable, allowing individuals to set it up to suit their seating position.
If the product is adjustable, this can be considered to be ‘inclusive design’, because a wide range of people will be able to use it.
My research into existing products and ergonomics, shows that adjustability is essential. The client said about one of the existing products, ‘I like the adjustability especially the height adjustment. This feature could be useful’.
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 43
SPECIFICATION POINT
ERGONOMICS: The ‘writing rest’ must be suitable for use with a wide range of easy chairs, and by the widest possible range of potential customers.
www.technologystudent.com © 2018 V.Ryan © 2018
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
https://www.facebook.com/groups/254963448192823/
FURTHER JUSTIFICATION
A writing rest that is only suitable for one or two easy chairs, will not be successful as a commercial product. It must ﬁt a range of easy chairs, so that it’s full commercial potential can be reached.
EVIDENCE FROM RESEARCH - JUSTIFICATION
The ‘ergonomics’ page shows a typical chair used by my main client. The dimensions / measurements of easy chairs are similar.
ERGONOMICS: The light should be adjustable, so that it can be focussed on the page being read by the user.
My main potential customer / client said, ‘ In addition, I need an adjustable light source, so that I can focus the light where I need it.’
Commonsense suggests that the light source should be fully adjustable. One setting is unlikely to suit all the potential customers.
SAFETY: The product must be safe to use, even when being adjusted.
Existing adjustable products have the potential to trap ﬁngers. This would not only be a design fault, but it may lead to the product having to be withdrawn from shops, due to health and safety concerns and concerns regarding litigation.
The existing writing rest shown on page 8 of my research, has a potential to trap ﬁngers. This must not apply to my design.
LIFE CYCLE AND SUSTAINABILITY: The
writing rest will be manufactured from sustainable materials such as recycled and reclaimed materials (aluminium, natural woods and recyclable plastics, including polypropylene). Also, the materials will be reclaimed at the end of it’s useful working life.
My research into existing products, shows that it is possible to manufacture the writing rest from recyclable materials, making the product a sustainable and environmentally friendly.
Using recyclable materials will enhance the environmental ‘credibility’ of the product. At the end of its life cycle, it will be dismantled and all possible materials up-cycled to new products.
A E S T H E T I C A P P E A R A N C E ( S H A P E ,
COLOUR, TEXTURE): The writing rest will be designed in a ‘Bauhaus’ style, as preferred by my main client.
The majority of the potential clients who completed the questionnaire elected ‘Bauhaus’ as the preferred style (see questionnaire results).
The writing rest will be a simplistic, functional and a thoughtful modern design. It will be modernist in appearance and be available in a range of colours The writing board will be distinctive and impressive to look at, as demanded by the Bauhaus style.
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 44
SPECIFICATION POINT
www.technologystudent.com © 2018 V.Ryan © 2018
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
https://www.facebook.com/groups/254963448192823/
EVIDENCE FROM RESEARCH - JUSTIFICATION
FURTHER JUSTIFICATION
QUALITY CONTROL, QUALITY ASSURANCE, PRODUCT TESTING: The components will be manufactured to the highest possible standard and checked for faults before assembly. The final product will be tested, for full functionality and overall quality of manufacture. The client will be asked to inspect the product and alterations made where necessary. The product will be guaranteed.
HEALTH AND SAFETY: Health and Safety regulations will be adhered to during the manufacturing process. When manufactured, the writing rest will be rigorously tested for safe use. British Standards and European Standards will be applied.
ADDITIONAL SPECIFICATION POINTS:
TIME SCALE AND PLANNING: The products design and manufacture will be completed within a two month period. The writing rest will be manufactured in three stages. First, a basic model will be made to help with the initial development of the product. This will be followed by a more sophisticated model, developed after customer and focus group discussion / feed back. Finally, after full development, the actual product will be manufactured to the highest quality standards.
This price includes materials and labour costs, tools and equipment requirements. A profit margin will be added by the retailer.
C O S T: T h e w r i t i n g r e s t w i l l b e ‘ b a t c h ’ manufactured on a production line, for £10 - £15.
My questionnaire research clearly ﬁnds that this is the most popular price range as determined by potential customers (see questionnaire).
https://www.facebook.com/groups/254963448192823/
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 45: CYCLE 2
THE DESIGN CONCEPT AND INITIAL IDEAS
HELPFUL LINK
1. DESIGN CONCEPT
www.technologystudent.com © 2018 V.Ryan © 2018
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
https://www.facebook.com/groups/254963448192823/
INITIAL LARGE NUMBER OF SKETCHES / IDEAS
CAD
7. INITIAL TESTING AND FEEDBACK
6. CHECK IDEAS AGAINST
THE SPECIFICATION
2
INITIAL MODELS
ENVIRONMENT / SUSTAINABILITY
http://www.technologystudent.com/despro_ﬂsh/iterative3.html

## Slide 46: GENERATING DESIGN IDEAS
Create (AO2)
HELPFUL LINK http://www.technologystudent.com/despro_ﬂsh/iterative3.html
AQA
AO2: Generating Ideas
Design & make prototypes that are ﬁt for purpose
AO3: Analyse & evaluate
OCR
CYCLE TWO COVERS THE EXAMINATION BOARDS ‘OBJECTIVES’ OUTLINED BELOW
Design and make prototypes that are ﬁt for purpose Critical thinking
EDEXCEL
  2.1 Design ideas
  2.2 Review of initial ideas
2.4 Communication of design ideas

## Slide 47
GENERATING IDEAS - AN INTEGRATED APPROACH
Generating a range of ideas should be achieved through employing a range of design tools, over a number of design sheets. Design is not always linear, such as, an ideas sheet followed by a CAD sheet, then health and safety etc... Designers usually work in an integrated fashion, with many areas appearing on an individual design sheet.
For example, a design sheet may include sketches, evidence of model making and testing, CAD, reference to the environment, experimentation, client/customer opinions and feedback and a even a summary of ﬁndings.
www.technologystudent.com © 2018 V.Ryan © 2018
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
https://www.facebook.com/groups/254963448192823/
GENERATING DESIGN IDEAS
HELPFUL LINK http://www.technologystudent.com/despro_ﬂsh/iterative3.html
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 48
THE NEXT TWO SLIDES SHOW A CHECK LIST OF DESIGN TOOLS, THAT COULD BE REGULARLY ‘TICKED’, AS PUPILS WORK THROUGH THE DESIGN AND DEVELOPMENT OF A PRODUCT.
THIS IS TO ENSURE THAT PUPILS USE A WIDE RANGE OF DESIGN TOOLS / TECHNIQUES, SUPPORTING ITERATIVE DESIGN
MOST TEACHERS WILL PRODUCE THEIR OWN CHECKLIST.
www.technologystudent.com © 2018 V.Ryan © 2018
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
https://www.facebook.com/groups/254963448192823/
https://www.facebook.com/groups/254963448192823/
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 49
CHECK LISTS - HAVE YOU MENTIONED OR INCLUDED THESE REGULARLY ?
The check list shown opposite,
can be used to ensure that students employ a wide range of skills and design strategies, when generating and developing ideas / designs.
A student places a tick against the statements in the check list, as and when he/she uses them. Most of the statements should have multiple ticks alongside, after the completion of a range of design sheets. Gaps may indicate a need to revisit design work.
Additional statements can be added, to suit the approach used by schools/ Design and Technology departments
INCLUDED PHYSICAL MODELS AND CAD MODELS
ADDED CUSTOMER / CLIENT VIEWS
USED SKETCHES, EXPLODED VIEWS, SECTIONAL VIEWS, ORTHOGRAPHIC PERSPECTIVE ETC...
APPLIED SIZES TO SKETCHES - LENGTH, HEIGHT AND DEPTH
EXPLAINED PROBLEMS FOUND WHILST SKETCHING / MODELLING
DESCRIBED MANUFACTURING PROCESSES: INJECTION MOULDING ETC...
INCLUDED COSTS TO MANUFACTURE ANDPRICE TO CUSTOMER
REFERRED TO THE SPECIFICATION REGULARLY
EXPLAINED METHODS OF CONSTRUCTION OF IDEAS
REFERRED TO PROPERTIES OF MATERIALS
MENTIONED ANTHROPOMETRICS AND ERGONOMICS
INCLUDED NOTES ON STYLE / AESTHETICS
HEALTH AND SAFETY ISSUES DISCOVERED AND RESOLVED?
INCLUDED A RANGE OF IDEAS?
SOLVED ANY PROBLEMS?
WHILE SKETCHING / MODELLING
CONTINUOUS EXPERIMENTATION AND TESTING
EVALUATED IDEAS AND MODELS
DISCUSSED ENVIRONMENT ISSUES
E.G. LIFE CYCLE - SUSTAINABILITY
USED CAD - COMPUTER AIDED DESIGN
DISCUSSED DISASSEMBLY OF IDEAS AND MODELS
INCLUDE PHOTOGRAPHIC EVIDENCE
E.G. WHEN TESTING MODELS
INCLUDE THE VIEWS OF OTHERS, INDIVIDUALS AND FOCUS GROUPS
DEMONSTRATE TECHNICAL UNDERSTANDING
INCLUSIVITY
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018
https://www.facebook.com/groups/254963448192823/
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 50: CHECK LISTS - HAVE YOU MENTIONED OR INCLUDED THESE REGULARLY ?
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018
www.technologystudent.com © 2018
ttps://www.facebook.com/groups/254963448192823/
CHNOLOGY TE
MENTIONED ANTHROPOMETRICS AND ERGONOMICS | 
INCLUDED NOTES ON STYLE / AESTHETICS | 
HEALTH AND SAFETY ISSUES DISCOVERED AND RESOLVED? | 
INCLUDED A RANGE OF IDEAS? | 
INCLUDED PHYSICAL MODELS AND CAD MODELS | 
ADDED CUSTOMER / CLIENT VIEWS | 
USED SKETCHES, EXPLODED VIEWS, SECTIONAL VIEWS, ORTHOGRAPHIC PERSPECTIVE ETC... | 
APPLIED SIZES TO SKETCHES - LENGTH, HEIGHT AND DEPTH | 
EXPLAINED PROBLEMS FOUND WHILST SKETCHING / MODELLING | ACHERS h
SOLVED ANY PROBLEMS? WHILE SKETCHING / MODELLING | 
CONTINUOUS EXPERIMENTATION AND TESTING | ATION OF TE
EVALUATED IDEAS AND MODELS | ORLD ASSOCI
DISCUSSED ENVIRONMENT ISSUES E.G. LIFE CYCLE - SUSTAINABILITY | W
V.Ryan © 2018
www.technologystudent.com © 2018
ttps://www.facebook.com/groups/254963448192823/
CHNOLOGY TE
DESCRIBED MANUFACTURING PROCESSES: INJECTION MOULDING ETC... | 
INCLUDED COSTS TO MANUFACTURE ANDPRICE TO CUSTOMER | 
REFERRED TO THE SPECIFICATION REGULARLY | 
EXPLAINED METHODS OF CONSTRUCTION OF IDEAS | 
REFERRED TO PROPERTIES OF MATERIALS | 
USED CAD - COMPUTER AIDED DESIGN | 
DISCUSSED DISASSEMBLY OF IDEAS AND MODELS | 
INCLUDE PHOTOGRAPHIC EVIDENCE E.G. WHEN TESTING MODELS | 
INCLUDE THE VIEWS OF OTHERS, INDIVIDUALS AND FOCUS GROUPS | ACHERS h
DEMONSTRATE TECHNICAL UNDERSTANDING | 
INCLUSIVITY | ATION OF TE
 | ORLD ASSOCI
 | W
V.Ryan © 2018

## Slide 51
THE NEXT THREE SLIDES PROVIDE LINKS TO IMPORTANT SKILLS, TECHNIQUES AND DESIGN STRATEGIES, THAT ARE REQUIRED THROUGHOUT THE DESIGN AND DEVELOPMENT PAGES OF THE PORTFOLIO.
THEY ARE CENTRAL TO ITERATIVE DESIGN.
THE LINKS MAY BE USEFUL, AS THEY LEAD TO A RANGE OF TECHNIQUES THAT STUDENTS CAN / SHOULD USE THROUGHOUT THE NEA.
https://www.facebook.com/groups/254963448192823/
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
www.technologystudent.com © 2018 V.Ryan © 2018
https://www.facebook.com/groups/254963448192823/
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 52
DRAWING AND SKETCHING SKILLS THAT COULD BE USEFUL FOR THE INITIAL IDEAS AND DEVELOPMENT
DURING CYCLE 2 (GENERATING IDEAS) THERE WILL BE A NEED TO APPLY A RANGE OF DRAWING AND SKETCHING SKILLS. THE LINKS BELOW MAY PROVE USEFUL WHEN DEVELOPING THESE NECESSARY SKILLS.
SHADING TECHNIQUES
http://www.technologystudent.com/despro_ﬂsh/graphics_shade1.html
PERSPECTIVE DRAWING
http://www.technologystudent.com/despro_ﬂsh/graphics_perspective1.html
ISOMETRIC DRAWING
http://www.technologystudent.com/despro_ﬂsh/graphics_iso1.html
ORTHOGRAPHIC DRAWING
http://www.technologystudent.com/despro_ﬂsh/graphics_ortho1.html
EXPLODED VIEWS
http://www.technologystudent.com/despro_ﬂsh/graphics_exviews1.html
THUMBNAIL SKETCHES
http://www.technologystudent.com/despro_ﬂsh/thumbnail1.html
http://www.technologystudent.com/designpro/thumbnail2.html CARD COMPOSITE DRAWINGS
http://www.technologystudent.com/designpro/drawtec5.htm
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 53
KEY AREAS / TECHNIQUES TO INCLUDE / COMMENT ON, DURING THE GENERATION OF IDEAS AND PRODUCT DEVELOPMENT
USING MODELS TO GENERATE AND TEST INITIAL IDEAS
http://www.technologystudent.com/despro_3/cardmod1.html http://www.technologystudent.com/despro_3/cardmod2.html http://www.technologystudent.com/despro_ﬂsh/prodevp4.html
http://www.technologystudent.com/despro_ﬂsh/graphics_model1.html
BLOCK MODELLING
http://www.technologystudent.com/despro_ﬂsh/graphics_block1.html THE ROLE OF A FOCUS GROUP IN HELPING TO GENERATE IDEAS
http://www.technologystudent.com/despro2/focgrp1.html WORKSHOP TESTING OF MATERIALS TO HELP GENERATE IDEAS
http://www.technologystudent.com/despro_ﬂsh/matsres2.html ENVIRONMENTAL FACTORS TO KEEP IN MIND
http://www.technologystudent.com/prddes1/lifecy1.html http://www.technologystudent.com/prddes1/life_energy1.html http://www.technologystudent.com/prddes1/closeloop1.html
http://www.technologystudent.com/prddes1/repair1.html
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 54
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018
KEY AREAS TO INCLUDE / COMMENT ON - DURING THE GENERATION OF IDEAS AND PRODUCT DEVELOPMENT
DURING CYCLE 2 (GENERATING IDEAS) THERE WILL BE A NEED TO EMPLOY DIFFERENT TECHNIQUES. THE LINKS BELOW MAY PROVE USEFUL WHEN DEVELOPING THESE NECESSARY SKILLS.
MATERIALS - THEIR THE PROPERTIES, METHODS OF JOINING AND MANUFACTURING PROCESSES
http://www.technologystudent.com/joints/joindex.htm
http://www.technologystudent.com/equip1/equipex1.htm
DESIGN MOVEMENTS AND DESIGNERS,
http://www.technologystudent.com/despro_ﬂsh/Designer1.html
QUESTIONNAIRES AD PICTOGRAMS - HOW TO USE IN THE INITIAL IDEAS
http://www.technologystudent.com/despro_ﬂsh/graphics_stats1.html
ANTHROPOMETRICS AND ERGONOMIC FACTORS
http://www.technologystudent.com/designpro/ergo1.htm

## Slide 55
FOLLOWING - ARE A SERIES OF DESIGN STRATEGIES, THAT WILL BE USEFUL TO PROMOTE DESIGN THINKING, BEFORE EMBARKING ON GENERATING IDEAS.
www.technologystudent.com © 2018 V.Ryan © 2018
https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018
https://www.facebook.com/groups/254963448192823/
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
V.Ryan © 2018

## Slide 56: DESIGN STRATEGY ONE GENERATE AN INITIAL DESIGN AND CONTINUE TO DEVELOPMENT
HELPFUL LINK http://www.technologystudent.com/despro_ﬂsh/basic_dev2.html
www.technologystudent.com © 2018 V.Ryan © 2018
https://www.facebook.com/groups/254963448192823/
Instead of producing an Ideas section followed by the Development section, combining both is an alternative approach. Each design sheet should start with an initial idea and include some development.
Produce at least 4 ideas / basic development sheets.
Each sheet should include CAD drawings or hand sketches (a combination of both CAD and sketches) of an idea from diﬀerent angles.
Add detailed notes to each sketch.
Show how you have developed your basic idea.
Then select 1 idea and produce 4 more pages of detailed development.
The idea below began with me selecting an existing product, from the range of images available on the Internet. You only need to like the basic / overall design and main features. It may be that you only like the shape. Once the basic idea has been selected, start sketching, adding features and functions as they occur to you, as you draw

## Slide 57: MEMPHIS STYLE MP3 PLAYER - IDEA 1
This is my initial design. It has two powerful speakers and is designed to look like ‘alert’ eyes. The design is symmetrical and can be positioned on almost any ﬂat surface.
I have added ‘retro’, 1960s styled legs. These will be adjustable, so that the height of the MP3 station, is level with a seated person. The legs add to the style and appearance.
I have increased the size of the lefthand speaker, to compensate for the shorter legs. Again, this is what you would expect of a Memphis style design.
Rubber stoppers could be ﬁxed to the underneath. These will protect any surface the MP3 station is placed on.
A range of colours are available.
A range of adjustable feet exist that would be suitable for my design.
I have altered the length of the legs, so that the left hand side is lower and the MP3 is at an angle. This makes it look unusual, rather like you would expect of a Memphis style.
The MP3 station will be supplied with a multi- coloured remote control.
I will develop the shape so that it is more ergonomic.
This an unusual design and it is ‘eye catching’.
I could consider using large springs in steady of normal legs. This will make the design even more unusual.
Casters could be an option for the customer, supplied in a range of colours.
They will be made from nylon which allows smooth ‘rolling’.
I will consider adding an ergonomic handle. This will be used to lift the left hand side of the MP3 station and the unit can then be moved, with the right hand legs resting on castors.
www.technologystudent.com © 2018 V.Ryan © 2018
https://www.facebook.com/groups/254963448192823/
I have used ‘real’ eyes to develop a simple colour scheme for the speakers
https://www.facebook.com/groups/254963448192823/
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 58
HELPFUL LINK http://www.technologystudent.com/despro_ﬂsh/devidea3.html
www.technologystudent.com © 2018 V.Ryan © 2018
https://www.facebook.com/groups/254963448192823/
DESIGN STRATEGY TWO GENERATING A DESIGN BY STARTING WITH
THE PROPERTIES OF A MATERIAL
One way of developing an idea for a product, is to consider the properties of a material ﬁrst. Select a material and list its physical properties. Then, select one or more properties and start designing.
EXAMPLE: Thin plywood can be forced to form a curve, but eventually it will split. Also, normal plywood tends to resist bending. However, ﬂexi-ply is composed of layers of thin plies. This means that it will bend into various 'curved' shapes, quite easily.
The material fact card opposite, outlines the basic physical properties of ﬂexi ply.
The 'ﬂexibility' of ﬂexi ply, allows a designer to develop an unusual product (see following design sheet).
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 59: MP3 PLAYER - IDEA 2
Retractable mains lead, retracts back into the column / stand automatically. It only extends to the amount wanted by the user. When unplugged, it winds back into the column automatically. This is a safety feature.
The cylindrical column is lightweight and lifts the speakers to a good ergonomic height for a seated user.
The column adds further, to the shape and form of the overall design, without over complicating it.
I have decided to select a material ﬁrst and then develop an initial design, based on the materials properties.
Flexi ply is a ‘ﬂexible’ form of plywood. It can be formed into ‘curved’ shapes with relative ease. It is quite light and strong. Plus, it has a natural wood ﬁnish.
Composed of several layers of thin plies.
I intend to use this property of ﬂexibility, to help me form an initial design / idea.
The curved layers of ﬂexi ply can be clearly seen. The ﬂexi ply has been formed into a shape that could not be produced by any other wood based product.
A jig could be made to hold the layers of ﬂexi
ply together whilst gluing.
I think this simple shape is aesthetically pleasing. It avoids sharp edges and corners.
The two speakers remind me of two giant eyes, staring forward, at the user.
The beech ﬁnish gives a light brown, grained ﬁnish. It is a natural ﬁnish and the materials can be recycled at the of its life cycle.
This is a compact unit, easy to handle and transport.
Relatively easy to disassemble at the end of its useful life time. The materials can then be recycled.
I have taken advantage of the natural ﬂexibility of ﬂexi ply to form an individual and unique design.
PLYWOOD BACK
FLEXI PLY BODY
PLYWOOD FRONT
SPEAKERS
CYLINDRICAL COLUMN
RETRACTABLE MAINS LEAD
I have added a base to ensure stability. It will stop the unit from ‘toppling over’, if knocked or pushed.
Simple large buttons have been added, to control the unit (inclusive design). They are ‘retro’ in style and very easy to use (ergonomically designed). The unit will also be sold with a sophisticated, programmable hand held control unit.
A docking station will be added to the top. This will be centrally located.
The unit is at a convenient and comfortable height for an average user.
CLIENT OPINION: My client likes this simple and yet stylish design. It could be manufactured within the budget allowed (£50). The products life cycle has been assessed and consequently, material that can be recycled has been used. It can be disassembled easily, as there are very few parts / components (with the exception of the electronic components). Overall, my client likes the style of the design.
450mm
400mm
www.technologystudent.com © 2018 V.Ryan © 2018
https://www.facebook.com/groups/254963448192823/
Flexi ply is a good electrical insulator. This means that the unit will meet and exceed electrical safety guidelines and regulations.
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/ www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 60
DESIGN STRATEGY THREE GENERATING A DESIGN BY STARTING WITH
AN ICONIC / INSPIRATIONAL DESIGN
www.technologystudent.com © 2018 V.Ryan © 2018
https://www.facebook.com/groups/254963448192823/
One good way of designing a new product, is to select a recognised iconic or well known design. Alternatively, you could select a design that inspires you. Then, redesign or develop it further, to incorporate new functions and features.
The E1027 Table was designed in 1929 and is still manufactured today. It looks as 'modern' today as it did when it was originally designed. It is another Eileen Gray piece of furniture, that has become a design icon/classic.
HELPFUL LINK http://www.technologystudent.com/despro_ﬂsh/devidea4.html
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 61: IDEA 3 - DEVELOPED FROM AN INSPIRATIONAL / ICONIC DESIGN
TELESCOPIC TUBES
HEIGHT PIN
Adjustable - 55 to 75cm
This is my ﬁrst design. This could be manufactured from stainless steel tube, although the diameter is larger than the original piece of furniture.
The speakers are inside the tube at the top.
I have designed the base so that it is more like a semicircle, rather the almost complete circle of the original iconic design.
Like the original design, the top tube can slide up and down the main vertical tube. It could even be designed so that it can revolve, without a need for the entire stand to revolve.
The original E1027 table had a pin on a chain to ﬁx the height of the table top. I have adopted the same technique. The stainless steel pin locks the adjustable speakers at the desired height.
Alternatively, I could use one of the locking devices seen below.
A transparent or translucent toughened glass table top could be placed above the speakers. This would mean that the speakers have an alternative or complementary function. My design now looks very similar to the original Eileen Gray design.
Small casters could be ﬁtted to the base, allowing easy movement around a room.
Another set of four speakers could ﬁt into the ends of the base, giving eight speakers in total.
My customer quite likes this way of selected an iconic design and then modernising it, by adding a speaker system.
The stainless steel tube can be recycled at the end of its life cycle. This also applies to the glass top. This makes the table / speaker system environmentally friendly and even sustainable.
I have added a second set of speakers (four speakers in total at the top).
The wide base ensures that the table / speaker system will be very stable and virtually impossible to knock over.
DOCKING STATION
ORIGINAL ICONIC / INSPIRATIONAL DESIGN
The E1027 Table was designed in 1929 and is still manufactured today. It looks as ‘modern’ today as it did when it was originally designed. It is an icon/classic design by the famous designer Eileen Gray.
An adjustable table composed of two ‘telescopic tubes’. These slide to the required height and a pin on a chain is used to lock them in position. High grade tubular stainless steel and tempered glass, provide a quality ﬁnish.
BOLTS WITH PLASTIC DECORATIVE COVER WING NUT
STAR HANDLE/ NUT
HANDLE BASED ON LIFT EYE
www.technologystudent.com © 2018 V.Ryan © 2018
https://www.facebook.com/groups/254963448192823/
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 62
HELPFUL LINKS
DESIGN STRATEGY FOUR
GENERATING A DESIGN USING THUMBNAIL SKETCHES
www.technologystudent.com © 2018 V.Ryan © 2018
https://www.facebook.com/groups/254963448192823/
Thumbnail sketches are simple outline drawings of initial ideas, for a product. Usually, they are not detailed, although they may be labelled or include brief notes. Limited colour is sometimes applied. The sketches are drawn relatively quickly, with a pencil, pen, felt pen or any media that the designer feels comfortable using.
Thumbnail sketches, allow the designer to be creative without worrying about detail. For example, there is no need to consider how materials will be joined or even what material can be used. In this way creativity can ‘ﬂow’ and ideas are put down on paper quickly. Thumbnail sketches are generally used in the early stages of the design process, although they are sometimes used when developing an idea.
http://www.technologystudent.com/despro_ﬂsh/thumbnail1.html http://www.technologystudent.com/designpro/thumbnail2.html
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 63: USING THUMBNAIL SKETCHES TO DEVELOP AN IDEA - IDEA 4
SPEAKER
MP3 STATION
The ‘back’ view shows the interlocking speaker and MP3 station system.
The design is based on the Memphis Design Movement. The speakers are rectangles / squares and they could be diﬀerent sizes and colours, producing an unusual design.
The distance of each speaker from the docking station, can be altered independently of each other.
SPEAKER
The system has a built in transformer, which means it can be plugged into a mains supply (240 volts). Batteries ﬁt into either base unit, providing power when playing the system outside.
SPEAKERS - DISTANCE EXTENDED
6 AA batteries are needed for use away from mains electricity.
Each speaker arm, can be altered to any angle between 0 to 90 degrees. This means that the sound can be directed in almost any direction, ideal for a party. If two people are sat at diﬀerent sides of a room, the speakers can be independently angles for perfect listening.
The MP3 station has two headphone sockets. This allows two people to listen to the same music, without disturbing other people in the room.
This is the ﬁnal ‘concept’ design. It clearly shows the Memphis inﬂuence. It is colourful, unusual and the speakers are diﬀerent sizes, although they deliver equal sound volumes.
The MP3 system is stable and very unlikely to be knocked over. It will be designed to conform to British and European safety standards.
SPEAKER ARMS
www.technologystudent.com © 2018 V.Ryan © 2018
https://www.facebook.com/groups/254963448192823/
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
This is my ﬁrst basic idea for an MP3 player. It is composed of three main parts, two speakers and a docking station.
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 64
HELPFUL LINKS
DESIGN STRATEGY FIVE GENERATING A DESIGN USING MODELS
www.technologystudent.com © 2018 V.Ryan © 2018
https://www.facebook.com/groups/254963448192823/
At any point during this design cycle, make models which will help you visualise your ideas, to test them out, to check the ergonomics and to show to potential customers. You may have other reasons to manufacture initial models. Take a photographic record of your models for your NEA.
http://www.technologystudent.com/despro_3/cardmod1.html http://www.technologystudent.com/despro_3/cardmod2.html http://www.technologystudent.com/despro_ﬂsh/prodevp4.html
http://www.technologystudent.com/despro_ﬂsh/graphics_model1.html
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 65: IDEA 5 - MP3 PLAYER / STATION - SCALED MODEL - SCALE 1:2
CORRUGATED CARD MODEL
I modelled one of my ideas using corrugated card. I made a rough model so that I could test my basic design.
The corrugated card was recycled from boxes and I found it ideal for the ﬁrst stage of modelling.
This is the front of my MP3 station. I added two disks that represent the speakers. They were made from the same corrugated card and painted. This helped me experiment with the positions of each speaker, the equaliser and controls.
I tried round buttons and used clipart as the graphic equaliser. I decided on the best arrangement for the buttons, speakers and equaliser and glued the parts together using PVA.
The body of the MP3 station was the most diﬃcult to make. The corners were made by folding each corner with the aid of a steel ruler and steel tube.
This gave the size of curve I needed. I used sellotape to hold the piece together. I quite like the width and height measurements, although I may alter the depth, so that it is slender in appearance.
When the main parts were ready, they were glued together, with the aid of a limited amount of sellotape. This helped me work out the number of parts I will need for the ﬁnal product.
This is the ﬁnal scaled model.
It measures 350mm X 130mm X 270mm. It is approximately half full size.
I like the basic design. Making the model helped me to think about all the parts I will need for the real product.
I like the basic shape, although I will need to think carefully about the ﬁnal colour scheme.
I could reﬁne the detail, possibly adding Art Deco or even Memphis features.
Making the model made me think about the materials I could use for the ﬁnal product. This design would be best suited to plywood including ﬂexiply, as it has all the properties I need.
The legs may need to be stronger and this could be achieved by adding another rail.
I cut the legs and supporting rail from a side of a corrugated card box. The slots in each side were cut with a craft knife. The three parts were glued together with PVA. The ‘through housing joint’ proved suitable for card and it will be suitable for the real product.
I used an image from the internet and glued it onto card, to make the MP3 player. When I place it on the top of the MP3 station, it will enable me to work out the best position for the customer (ergonomic design).
My ﬁrst scaled model sitting on a work bench. This shows the size of the model.
Basic equipment needed for making the model.
PVA, sellotape / double sided tape and craft knife and safety ruler.
A focus group composed of other pupils, suggested putting the buttons on the top, making it easier to access them. It was suggested that legs may not be needed, but they could be an option. The MP3 player may be more popular if it was supplied in a range of colours.
FOCUS GROUP SUGGESTIONS
FRONT
LEGS
BACK
BODY
Go to http://www.technologystudent.com/designpro/despro1.htm
for detailed information on the iterative design process including model making.
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2017 V.Ryan © 2017
https://www.facebook.com/groups/254963448192823/
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
www.technologystudent.com © 2017 V.Ryan © 2017

## Slide 66
HELPFUL LINKS
DESIGN STRATEGY SIX
DEVELOPING A DESIGN FROM A THEME
HOW TO INCORPORATE THE STYLE OF A WELL KNOWN DESIGNER IN A FINAL DESIGN
www.technologystudent.com © 2018 V.Ryan © 2018
https://www.facebook.com/groups/254963448192823/
Product designers sometimes select features from a design movement or the work of a known designer, and apply them to their own designs. For example, the work of Charles Rennie Mackintosh has many recognised features. Some of the features he developed are regularly applied to modern designs. He used stain glass and ceramic tiles as decoration. Mackintosh utilised a combination of design principles derived from Art Nouveau, the Arts and Craft Movement and Japanese design. Many of his designs are regarded as examples of early modernism.
http://www.technologystudent.com/designpro/devtheme4.html http://www.technologystudent.com/designpro/devtheme1.html
http://www.technologystudent.com/designpro/devtheme2.html
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 67
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018
DEVELOPMENT SHEET - HOW I INTEND TO INCORPORATE MY CHOSEN DESIGN THEME IN MY FINAL DESIGN
THEME - CHARLES RENNIE MACKINTOSH
Argyle Chair 1897
Hill House Chair 1903-1903
INGRAM CHAIR 1903
High Back Chair 1899
SHAPES FROM SEAT BACKS
MACKINTOSH ROSE TILE
My DVD / CD storage unit has many of the features seen in the designs of Charles Rennie Mackintosh. The storage unit will have a stain glass back. Mackintosh style ceramic tiles will be positioned on the top. Slots, similar to those seen in his chair designs, will also feature on the sides of the storage unit.
FEATURES:
DEVELOPING MY DESIGN:
MACKINTOSH FEATURES
+ +
Charles Rennie Mackintosh was an architect and interior designer from the late Nineteenth and early Twentieth Century. He designed several classic chairs. I have identified the parts that I like, and I intend to incorporate these features in my storage design.
I intend to use stain glass and ceramic tiles, inspired by Charles Rennie Mackintosh.
STAIN GLASS AND CERAMIC TILE DESIGNS
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018
https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 68
FEATURES:
THEME - ART DECO
DEVELOPING MY DESIGN:
My favourite design period is Art Deco. It was an era of ornate style and decadence and style. Designs from this era exhibits geometrical shapes, substantial angles and generous curves. They also displayed subtle and delicate features and colour schemes.
These are two typical Art Deco patterns. Art Deco patterns tend to have: distinctive circular patterns, bold straight lines and subtle use of colour and shade. They often look rather abstract.
I like the way chromed steel tube has been used and I will apply a similar geometrical shape to may design
I have taken a geometrical pattern and colour scheme, typical of Art Deco and applied to the table top.
The overall colour scheme is taken from some of the sample Art Deco designs drawn opposite.
Greys and blues
dominate
Circle taken from the chair design and incorporated in the table top.
Painted shelve. pattern taken from a popular 1930s Art Deco pattern.
I have tried to keep this design in keeping with the Art Deco style. Geometrical shapes, the use of chromed steel, a subtle colour scheme with a touch of ‘modernism’, have been included to deliver a distinctive design.
DEVELOPMENT SHEET - HOW I INTEND TO INCORPORATE MY CHOSEN DESIGN THEME IN MY FINAL DESIGN
www.technologystudent.com © 2018 V.Ryan © 2018
https://www.facebook.com/groups/254963448192823/
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 69
NOW IT IS TIME TO PRODUCE 5 TO 8 DESIGN SHEETS OF INITIAL IDEAS. EACH SHEET SHOULD DISPLAY A RANGE OF TECHNIQUES AND STRATEGIES. A VARIED RANGE OF DESIGNS SHOULD BE PRESENTED.
REMEMBER - A COMPLETE NEA PORTFOLIO SHOULD BE APPROXIMATELY 20 SHEETS
www.technologystudent.com © 2018 V.Ryan © 2018
https://www.facebook.com/groups/254963448192823/
https://www.facebook.com/groups/254963448192823/
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 70
CYCLES 3 and 4
HELPFUL LINK http://www.technologystudent.com/despro_ﬂsh/iterative4.html
1. ONE IDEA TO BE FULLY DEVELOPED.
2. FINAL DRAWINGS
3. FINAL PROTOTYPE MANUFACTURED
4. FULL TESTING BY FOCUS GROUP AND CLIENT
5. FINAL EVALUATION AGAINST SPECIFICATION
6. FINAL IMPROVEMENTS AND MODIFICATIONS
4
3. MATERIALS TESTING
1. IMPROVEMENTS TO SELECTED DESIGNS
5. TESTING OF 3D PROTOTYPES
7. INITIAL EVALUATION / CONCLUSIONS
6. CLIENT / TARGET MARKET
INPUT / FEED BACK
2. FOCUSSED ANTHROPOMETRIC
RESEARCH, LEADING TO ERGONOMIC DESIGNS
3
4. ENVIRONMENT / SUSTAINABILITY
DEVELOPING DESIGN IDEAS TO ONE FULLY DEVELOPED IDEA
www.technologystudent.com © 2018 V.Ryan © 2018
https://www.facebook.com/groups/254963448192823/
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 71: CYCLES THREE AND FOUR COVERS THE EXAMINATION BOARDS ‘OBJECTIVES’ OUTLINED BELOW
DEVELOPING DESIGN IDEAS - IMPROVEMENTS TO SELECTED DESIGNS
AQA
A02: Design & make prototypes that are ﬁt for purpose Developing design ideas
A03: Analyse & evaluate
OCR
Development of design ideas into a chosen design
Critical thinking
Demonstrate and apply knowledge and understanding of – technical principles, designing and making principles
A03: Analyse & evaluate
EDEXCEL
2.3 Development of design ideas into a chosen design
  2.4 Communication of design ideas
  2.5 Review of chosen design
4.1 Testing and evaluation

## Slide 72
CYCLE 3 and 4: IMPROVEMENTS TO SELECTED DESIGNS LEADING TO ONE FULLY DEVELOPED IDEA
HELPFUL LINKS
By now the student will have produced several design sheets containing a range of initial ideas. Students will have used a range of ‘design tools’ such as, client feedback, focus group discussions, surveys, model making, diﬀerent presentation techniques etc.....
Select two or three ideas for further development. This will involve more detailed drawings, models, feedback, testing etc...( a range of design tools).
www.technologystudent.com © 2018 V.Ryan © 2018
https://www.facebook.com/groups/254963448192823/
http://www.technologystudent.com/despro_ﬂsh/iterative4.html http://www.technologystudent.com/despro_ﬂsh/iterative5.html
http://www.technologystudent.com/despro_3/integrate1.html http://www.technologystudent.com/despro_3/integrate2.html http://www.technologystudent.com/despro_3/integrate3.html http://www.technologystudent.com/despro_ﬂsh/prodevp4.html http://www.technologystudent.com/despro_ﬂsh/prodevp5.html
http://www.technologystudent.com/despro_ﬂsh/prodevp6.html http://www.technologystudent.com/despro_ﬂsh/prodevp7.html http://www.technologystudent.com/despro_ﬂsh/prodevp8.html
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 73
NEXT ARE TWO SAMPLE DESIGN SHEETS, SHOWING THE DEVELOPMENT OF THE MP3 PLAYER SHOWN ON EARLIER SLIDES.
TAKE PARTICULAR NOTE OF THE MANUFACTURING SPECIFICATION, AS SOME EXAMINATION BOARDS EXPECT TO SEE THIS SHEET, REFLECTING THE FINAL DESIGN.
www.technologystudent.com © 2018 V.Ryan © 2018
https://www.facebook.com/groups/254963448192823/
https://www.facebook.com/groups/254963448192823/
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 74
PUPIL/PERSON | A
Person A | 1350mm
Person B | 1490mm
Person C | 1520mm
Person D | 1400mm
Person E | 1390mm
Person F | 1350mm
Person G | 1420mm
Person H | 1470mm
Person I | 1380mm
Person J | 1480mm
Person K | 1400mm
Person L | 1350mm
TOTAL(S) | 17000mm
AVERAGE | 1416mm
think will appeal to a wide range of customers.
The speakers are the same size but the speaker casings / housings vary. However, they appeal visually, the speakers are in a ratio of 3:4.
KNOCK DOWN JOINT
This knock down joint is a
possibility. It will provide a reasonably strong joint, although it will take ﬁve minutes to assemble each corner.
COLOUR SCHEME
The colour wheel shows the range of colour schemes available to potential customers. Customers can select from a range in a shop or from the online website.
I have decided on bright, lively colours, that reﬂect the Memphis Design Movement.
SELECTED IDEA FOR FURTHER DEVELOPMENT
This is the idea that I will develop further. It is a simple design that I
COUNTERSUNK SCREWS
Brass countersunk screws will be used to ﬁx the back board in position. This will be the ﬁnal stage of speaker assembly. Screws will be used, so that repairs can be carried out, if necessary.
P
A
V
PVA will be used to permanently ﬁx the speaker frame to the body.
Alternatively, contact adhesive could be used.
BODY
SPEAKER FRAME
BACK BOARD
SPEAKER
JOINTS AND FITTINGS
THROUGH DOVETAIL JOINT
If a customer requests a superior, hand made speaker system, dovetail joints will be used. This will take far longer than all the other proposed joints, but it looks better and is much stronger.
DOWEL JOINT
Dowel joints are quick and easy to construct, especially using a template to line up the dowels with the holes.
This is the most likely joint, as it is strong and quick to construct. This joint is the most cost eﬀective method.
ERGONOMICS
1416mm
My speaker system is designed to be positioned at hearing level. This allows the listener to hear the clear digital music. See table of results
When playing at a party or to more than one person, the speakers can be angled, to project the sound over a wider area.
A headphone jack plug is also available, for personal comfort and
quiet listening.
The system is designed to be lightweight, allowing safe movement and transport.
The MP3 station is designed to be strong enough, to be carried in one hand.
When the speakers are folder back, the entire system becomes entirely transportable.
Tracks can be loaded directly onto the station, so that music can be played, whilst the system is carried.
www.technologystudent.com © 2018 V.Ryan © 2018
https://www.facebook.com/groups/254963448192823/
TRANSPORT
An unexpected bonus of the folding speaker system, is the convenience of storage. When folded right back, the entire system forms a cube. This is ideal if the system is stored each night, or put away for security.
RUBBER FEET / STOPPERS
Cheap rubber feet will be ﬁxed to the MP3 station, to ensure that it does not damage any surface it is placed on.
The feet absorb vibration from the speakers, giving a deeper and purer sound.
https://www.facebook.com/groups/254963448192823/
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 75: MY MANUFACTURING SPECIFICATION
SCALE OF PRODUCTION AND
PRODUCT DESCRIPTION
FINAL IDEA
ASSEMBLY AND CONSTRUCTION
COUNTERSUNK SCREWS
P
A
V
BODY
SPEAKER FRAME
BACK BOARD
SPEAKER
THROUGH DOVETAIL JOINT
Pin hinges
Two Speaker Grills
Liteair Speakers
Panel pins
PVA Glue CSK
screws
One oﬀ / Prototype:
Continuous Production:
Batch Production:
Just In Time:
THE MANUFACTURE OF MY PRODUCT
Choose one of the industrial scales of manufacturing listed below. Explain how it has inﬂuenced the design and manufacture of your product.
standard components. The way it is assembled has
at the end of its useful life.
STANDARD COMPONENTS TO BE USED DURING MANUFACTURING
My speaker system is aimed at teenagers. The design has been inﬂuenced by the Memphis
Design Movement. It is brightly coloured and
unusual in shape and form.
It has been designed so that it folds up and can be carried from one location to another.
My speaker system will be batch produced, when it is Recycleable and sustainable materials will be
manufactured in a factory. Consequently, it can be used, so that it is as environmentally friendly as
assembled easily with screws, panel pins and other possible.
been simpliﬁed, so that it can be put together quickly. Standard components will be used to reduce
Readily available materials such as MDF will be used. development and manufacturing costs and the
It is designed to be disassembled easily for recycling, ﬁnal price to the customer.
AND MY PRODUCT
I will set up a quality checking system, to ensure that the product is manufactured to the highest possible standards.
Materials will be visually checked, so that only the best materials are used. Materials with imperfections will be rejected / recycled. The materials will be tested for strength and durability, before the manufacturing process begins.
The quality of manufacturing will be checked at every stage, with faults being identiﬁed and corrected.
The ﬁnished product will go through extensive tests and checks, before being passed on to the customer.
The exploded drawing shows the assembly / construction of each of the speakers. Standard components and manufactured parts are combined to produce the mp3 system.
www.technologystudent.com © 2018 V.Ryan © 2018
https://www.facebook.com/groups/254963448192823/
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018
QUALITY ASSURANCE/ CONTROL

## Slide 76
NEXT IS A MATERIALS TESTING SHEET. IT MAY BE NECESSARY FOR STUDENTS TO TEST MATERIALS. HOWEVER, IT MAY ONLY BE NECESSARY TO USE ONE OR TWO OF THE TESTS AND THESE CAN BE INTEGRATED WITH OTHER DESIGN WORK. THERE MAY NOT BE A NEED FOR A SEPARATE MATERIALS TESTING SHEET.
HELPFUL LINKS
PROPERTIES OF MATERIALS
http://www.technologystudent.com/joints/matprop1.htm
http://www.technologystudent.com/joints/matprop2.htm
MATERIALS TESTING
http://www.technologystudent.com/joints/htest1.html
http://www.technologystudent.com/joints/tensile1.html http://www.technologystudent.com/joints/conduct1.html
http://www.technologystudent.com/joints/toughness1.html
www.technologystudent.com © 2018 V.Ryan © 2018
https://www.facebook.com/groups/254963448192823/
https://www.facebook.com/groups/254963448192823/
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 77
MATERIALS TESTING
SHEET
NAME:
I carried out a hardness test on samples of perspex, pine, aluminium and steel. These are materials that I may use, when manufacturing my speaker system /
MP3 station.
I tested each piece of material, to determine if any
are suitable for my project.
The ‘slug’ was loaded at the top of the tube and
released, so that it impacted the sample material
below.
I recorded the results in the table below.
HARDNESS TEST
0.00v
CONDUCTIVITY TEST
I carried out a simple conductivity test on the samples. The only insulator was perspex.
The volt meter showed that it did not conduct electricity current at all.
Perspex will also oﬀer protection from 240 volts main electricity and batteries
DRILLING TEST
I drilled each sample with a 4mm bit, using a bench drill.
The most diﬃcult to drill was the steel, as it created sharp swarf.
The perspex had to be protected with masking tape, in case it shattered. It drilled relatively easily, but with care.
The pine drilled easily but created dust.
MATERIAL | RESULT | DESCRIPTION
PERSPEX | FAIR | MEDIUM SURFACE DAMAGE
PINE | FAIR | DEEP INDENT MINIMUM SURFACE DAMAGE
ALUMINIUM | GOOD | MINIMUM SURFACE DAMAGE
STEEL | GOOD | MINIMUM SURFACE DAMAGE
RESULTS
SUMMARY
All these materials are suitable for my product, as they will resist knocks and drops.
I carried out further hardness tests on the range of materials, using a centre punch and a ball pein hammer.
Although not a scientiﬁcally accurate test, all the materials performed well.
In order of hardness - steel, aluminium, perspex and pine.
These results conﬁrm the ﬁndings of the hardness test above.
WEIGHT TEST
I weighed the samples. The results clearly showed pine weighing less than all the other materials.
STEEL PERSPEX ALUMINIUM PINE
I will consider using pine for the casing of my MP3 station, although both perspex and aluminium are possibilities.
Steel is the least likely to be used.
MATERIAL | RESULT | DESCRIPTION
PERSPEX | MODERATE | TENDENCY TO SPLIT, IF MASKING TAPE NOT USED
PINE | EASY | EASY TO DRILL, DUST/CHIPPINGS CREATED
ALUMINIUM | MODERATE | SOFT METAL, EASY TO DRILL WITH CARE
STEEL | DIFFICULT | DIFFICULT TO DRILL, CREATES SHARP SWARF
FILING TEST
The steel was the hardest to ﬁle and required a lot of eﬀort. The ﬁnish was relatively smooth although teeth marks could be seen.
The pine ﬁled easily, although it did not produce a good ﬁnish.
The aluminium ﬁled easily as well. The ﬁnish was quite good. Teeth marks could be seen.
The perspex ﬁled easily and the ﬁnish was reasonably smooth.
SMOOTHING / FINISH TEST
I used wet and dry paper / glass paper to ﬁnish a side of each sample. All produced a good ﬁnish, smooth to the touch. The hardest material to smooth was steel, because it took longer than the other materials. Steel will rust if the surface is not protected with paint or lacquer.
Any of these materials will give the ﬁnish I need for my project.
www.technologystudent.com © 2018 V.Ryan © 2018
https://www.facebook.com/groups/254963448192823/
https://www.facebook.com/groups/254963448192823/
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 78
THE FOLLOWING TEN DESIGN SHEETS SHOW THE DESIGN AND DEVELOPMENT OF AN INNOVATIVE ‘TAPE’ MEASURE. A RANGE OF DESIGN TOOLS HAVE BEEN USED ON THE DESIGN SHEETS.
AS A BASIC GUIDE - THE FIRST 4/5 DESIGN SHEETS SHOW A RANGE OF IDEAS, THEN ONE OR TWO ARE SELECTED FOR FURTHER DEVELOPMENT, WITH ONE FINAL DEVELOPED IDEA BEING SELECTED, RESULTING IN A WORKING DRAWING.
THIS SELECTION OF DESIGN SHEETS IS A SAMPLE OF ITERATIVE CYCLES 2, 3 AND 4 (WITHOUT THE FINAL TESTING AND EVALUATION)
www.technologystudent.com © 2018 V.Ryan © 2018
https://www.facebook.com/groups/254963448192823/
https://www.facebook.com/groups/254963448192823/
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 79
This is a standard design of a basic tape measure. The
clip has been designed to grip a belt. The tape rewinds automatically,
but in this case too quickly (health and safety issue).
The tape tends to develop faults, after it has been used several times.
These are alternative tape measure ‘ends’.
A has a small ‘lip’ that grips the underneath of the materials being measured.
B has a magnetic end that attaches ﬁrmly to steel.
underneath the casing and the thumb holds the top ﬁrmly.
Below the ergonomic shape is clearly seen. The top and underneath have a rubber layer, to make the tape more
comfortable to hold. In addition, it provides
drops
This ‘grip’ has small ‘suckers’ to hold the tape in place
A.
B.
GRIP
MAGNET
CASING
BELT CLIP
RUBBER GRIP
This design has a magnetic base, allowing a secure ﬁx to steel products and materials. This means that it is unlikely to slip, when in use on steel.
CASING
The transparent casing of this design, means that the internal workings / mechanism can be seen. This is an aesthetic feature. Also, the tape measure can be read easily, through the casing.
LENS VIEW
LENS
TRANSPARENT CASING
This is a ‘radical’ developed design, with the steel tape being replaced by a distance sensor. A small
reﬂector is placed at one end of the material and the main body of the tape measure at the other end. The ‘device’ calculates the precise distance between the body and
the reﬂector. A low power laser is used for safety reasons.
The distance is digitally displayed in a small LCD screen.
Reﬂector showing laser bouncing back to the tape measure body.
A back light allows use in dark spaces or poor light conditions.
The transparent body has been developed a little further. It is a more ergonomic design. The body has a built in lens, which magniﬁes the scale, allowing easy reading of the measurement.
The grip on the casing slides up and down. Once the tape is retracted into the casing, the grip can also be retracted, allowing easier storage. No sharp edges visible.
This undated design has two grips, one at the end of the tape and the other on the casing of the tape measure. this is unlikely to slip, when in use.
PRESSED STEEL CASINGThe casing shape has been
ergonomically redesigned, so that it can be held in the
hand comfortably.
The ﬁngers grip
TRANSPARENT POLYCARBONATE CASING
RUBBER SUCKERS
AESTHETICALLY PLEASING
Symbol applied to all these
improved protection against knocks and designs. All materials from
a recycled source and can be recycled again.
Manufactured from recyclable polycarbonate.
55mm
55mm
55mm
RUBBER ‘COMFORT’ CURVE
INJECTION MOULDED
LIFE CYCLE
All designs have a life cycle - a guaranteed for ﬁve years.
PRODUCT DEVELOPMENT
SHEET 1
NAME:
MAGNETIC
Ergonomic design, for
comfort and ease of use GRIP
GRIP
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
This design has improved grip, as the underneath of the tape measure is rubber and has ‘teeth’. This design is less likely to slip on the material it is being used to measure.
www.technologystudent.com © 2018 V.Ryan © 2018
https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 80
PRODUCT DEVELOPMENT
SHEET 2
NAME:
LIGHT/DARK SENSOR
This is a reﬁned design. An LED light illuminates the scale on the tape. As the tape is ‘extended’ the light is automatically turned on.
Alternatively, a light / dark sensor, incorporated in the casing, turns the LED light on, when the light level drops.
The slide lock, prevents the tape from winding back into the casing.
The clear side panel is illuminated, when the main LED is in operation. This allows the internal mechanism to
be seen and is an aesthetic feature.
These are an early development of the writing style. This will clearly identify the manufacturer or trade name.
The style must reﬂect the quality / high standard of manufacture.
An ultra bright LED will provide enough light to illuminate the scale. The circuit will be powered by two 1.5v button / coin batteries. The batteries will be replaceable.
LENS
GRIP
TRADE NAME
RUBBER COMFORT CURVE
The product can be manufactured in a range of colours. Blue seen above.
This design includes a colourful casing and a circular transparent HIPs window. The rotating
mechanism can be seen and it is illuminated when the tape is extended. A lens magniﬁes the
scale.
GRIP
TRANSPARENT WINDOW
LED
LENS
DISASSEMBLED BASIC TAPE MEASURE
ASSEMBLY SCREWS
TRANSPARENT WINDOW
BOTTOM RUBBER GRIP
The drawing above, shows the disassembled casing. The two sides are held together by small M4 countersunk screws. This allows for repairs to be carried out and for the coin batteries to be replaced.
Industrial strength double sided tape, permanently holds the rubber bottom grip and the rubber comfort curve, to the casing.
RUBBER COMFORT GRIP
INDUSTRIAL STRENGTH MASKING TAPE
A
C
The casing has an additional ‘lug’, which has been drilled. A small loop of leather / textile material can be used to hold the tape measure, from a standard hook.
A hook has been formed, as part of the casing. The hook has been positioned so that the tape measures centre of gravity, allows it to hang securely.
A small magnet on the casing, allows the tape measure to be held securely underneath any steel workshop shelf.
TWO PLASTIC RIVETS
Steel, aluminium and even copper rivets could be used to secure the grip to the tape.
The rubber grip is attached to the base of the tape measure, with either glue or industrial standard, double sided tape. It prevents the casing slipping, when the measure is in use.
LED
CIRCUIT
BUTTON BATTERIES
The grip at the end of the tape, could be attached permanently to the tape by colourful plastic rivets. these will be an attractive feature. Even luminous rivets could be used, making the grip more visible.
GRIP
LUG
HOOK
MAGNET
https://www.facebook.com/groups/254963448192823/
STORAGE HOOKS
B
www.technologystudent.com © 2018 V.Ryan © 2018
https://www.facebook.com/groups/254963448192823/
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 81
PRODUCT DEVELOPMENT
SHEET 3
NAME:
An ultra bright LED shines directly on to the scale portion of measuring tape. The
lens, enlarges the scale reading, so that it is easy to read.
The rotating tape mechanism, can be seen inside the casing. It is illuminated when the LED turns on.
The extent of the rubber comfort grip can be seen, the average width of the palm of the hand.
The CAD drawing, allows the design to be viewed as a realistic model.
LED
MAGNIFYING LENS
RUBBER COMFORT GRIP
TRANSPARENT VIEWER
This CAD drawing clearly shows how the lens magniﬁes the scale. The red ‘datum’ line, identiﬁes the measurement precisely.
The rubber grip, at the base of the tape measure, has ‘teeth’, that grip the material it is placed on.
ILLUMINATED POLYCARBONATE WINDOW
RUBBER COMFORT GRIP
This CAD exploded drawing, shows how the basic design looks when disassembled. I showed this to the focus group, to explain my initial thoughts about joining the various parts. They suggested developing a friction ﬁt casing,
MAIN CASING rather than relying on small screws.
STORAGE HOOK
PLASTIC RIVETS
TAPE RUBBER GRIP
MEASURE
INTERNAL MECHANISM
SIDE
POLYCARBONATE WINDOW
SAMPLE FASHIONABLE COLOURS
TYPICAL TRADITIONAL The casing could be manufactured TAPE MEASURE in a range of colours. Four
fashionable samples are seen opposite. My design will not be traditional, but will reﬂected the fact that many tape measures are bought and used by people to carry out DIY at home. The design uses popular colours, not only more traditional colours, used in industry.
I LIKE IT!
IT COULD BE BETTER
COLOURFUL
COMFORTABLE
WILL IT WORK?
WHAT COST?
The CAD drawings below, show the diﬀerent types of storage ‘hooks’ I am considering. My favourite is the magnet, because of its simplicity and because it will secure the tape to a steel shelf, piece of steel equipment or steel tool box.
www.technologystudent.com © 2018 V.Ryan © 2018
https://www.facebook.com/groups/254963448192823/
PLACE PHOTOGRAPH HERE
The LED light could be one of several colours. This means that the light emitted from the clear
window could be colourful, as well
a functional.
A vinyl cutter could be used to manufacture the lettering / logo for the
tape measure.
Alternatively, I will consider some form of engraving, possibly by a laser cutter.
Vacuum forming the casings for the tape measure, seems a good manufacturing option at this stage. It will certainly work well for the prototypes and models. Both the main casing and the side, could be designed to ﬁt tightly together, forming a friction ﬁt. This would avoid the need for small screws.
My Focus Group, discussed the ﬁrst design and viewed the CAD model. They quite liked it, especially the ergonomics and the comfortable handling. They suggested that I should develop the circuit, battery replacement, make real models and consider how the parts will be manufactured.
MATERIALS: Polycarbonate has good impact resistance properties, especially when combined with rubber. Alternatively, I will consider kevlar for the casing with an elastonomer for the ‘rubber’ grip. The elastonomer, will combine the strength of plastic, with the ﬂexibility of rubber.
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 82
PRODUCT DEVELOPMENT
SHEET 4
NAME:
I made a series of basic models, from MDF and High Density Polystyrene. This allowed me to experiment with the initial shape. I changed the shape of idea 1 slightly as a result of cutting the material. See below, compared to the original sketch
I also changed the proportions of each part of idea 2, when I started to draw the basic design on to the MDF.
I made the idea slightly higher, to accommodate the rubber hand grip. This gave the tape measure a more balanced look.
Applying colour and shade to each of
the MDF models, allowed me to judge
how the colour scheme enhanced to model and how it may look on the full sized product. Brighter, less traditional colours were more appealing.
The basic models helped me reﬁne the ‘ergonomics’. I handled the models and tried them out, in the normal tape measure holding position.
The ﬁrst idea was less comfortable than the ‘rubber gripped’ second idea.
Using the sanding disk, I was able to experiment with the shape of the ‘grip’, until it felt comfortable. I tried ﬁling by hand, to produce individual ﬁnger grips. This added to the time of manufacture and did not feel any more comfortable.
Modelling helped me arrive at an
ergonomically pleasing shape. It was
comfortable to hold and could be held securely when the tape was in use.
I was able to test each of the colours suggested on previous design sheets.
They are all suitable.
The shape arrived at through modelling, is taller, as the model was more aesthetically pleasing, when altered.
Drawing the scale on to the polystyrene modelling material, made me consider the type of scale that should be used. It is possible to manufacture the tape, so that there are alternative scales (CM, mm, imperial etc...) The customer could choose which scale suited him/her.
A potential customer tested the completed model. He like the potential for a soft grip and the holding position. However, he felt the bottom grip may not be completely eﬀective, when the tape measure is in use.
The rubber grip at the bottom of the casing looks good, but when tested it tended to slip. This was due to the tape measure being lightweight.
An alteration is sketched opposite.
A potential solution is to add a ‘hook’ to the bottom of the tape measure casing. This could be used to hook on to the opposite end of the material being measured. The combination of the rubber grip and hook, may ensure the tape measure does not slip when being used.
HOOK
My sketch on graph paper, showing an added hook.
www.technologystudent.com © 2018 V.Ryan © 2018
https://www.facebook.com/groups/254963448192823/
https://www.facebook.com/groups/254963448192823/
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
www.technologystudent.com © 2018 V.Ryan © 2018
I altered the rubber grip so that it was smoother, see sketch opposite.

## Slide 83
PRODUCT DEVELOPMENT
SHEET 5
NAME:
The model tape measure seen in the photograph below gave positive results. The casing felt comfortable in the hand. The rubber top and bottom grips feel comfortable due to the shape.
The position of a sensor or a mechanical switch, to turn on
the LED light, will need to be considered. The ergonomic design will need to ensure that the ‘switch’ can be reached and operated easily.
The tape measure has been modiﬁed to include a push button switch. This can be activated easily, by one ﬁnger. Easy and simple switching on and oﬀ of the LED is the result.
A possible problem, is that the switch could be pressed by accident, far too easily.
PUSH BUTTON SWITCH
SLIDE SWITCH
A slide switch requires a positive on and oﬀ. This type of switch is likely to be activated by accident.
LIGHT/DARK SENSOR
A light / dark sensor could automatically turn on the LED, when illumination is required. However, a ‘master’ switch will be needed, as the LED will come on when the tape measure is placed in a bag, for instance.
The reﬁned design below, is a result of testing the model. The small change to the top rubber grip, allows the ‘thumb’ to ﬁt into the grip. This is even more comfortable and means the tape measure can be held even more securely.
THUMB GRIP
This colour rendered sketch, gives a relatively accurate view of the amended design.
The thumb grip has been added. In addition to the ergonomics being improved, the
tape measure is more aesthetically pleasing.
60mm
70mm
Testing the model highlighted a problem. The tape dis not ﬂat on the surface of the material being measured. It is slightly raised, making the measurement inaccurate.
The grip at the end of the tape does its job and allows the tape to be pulled out of the tape measure casing.
95mm
The ‘tape’ was level, when the end grip ‘sat’ on top of the material, rather than gripping.
Developing an new type of end grip, that securely sits on top of the material, may be the solution.
RIVETS/PINS
One possible solution, is to redesign the end grip. The one shown below has been
modiﬁed to hold the tape level with the
material and at the same time, grip the end of the material securely.
Retractable grip. Can be pulled out of the base, when required.
CLOSED
www.technologystudent.com © 2018 V.Ryan © 2018
https://www.facebook.com/groups/254963448192823/
OPEN
UPDATE - Most tape measures automatically retracted back into the casing, when the tape is released from the edge of the material. However, the tape measure could be designed, so that the tape stays extended automatically and has to be released by pressing a button (working in the opposite way).
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 84
PRODUCT DEVELOPMENT
SHEET 6
NAME:
7 8 6 7 8
1 5 3 7
1 1 3 1 5 3 7
2 8 4 8 3 8 4 8 2 8 4 8 4
8.88cm 3.48inch
88.88mm
3.48inch
The function buttons will allow easy selection of various features. Each function button will be allocated a dedicated feature.
The buttons have been positioned so that they cannot be ‘knocked’ accidentally.
Metric and imperial tape measure. Allows measuring via the two tapes and a digital display.
SELECTION OF SCALES
The lens facility ensures that reading the scale is easy, and helps in poor light conditions
Both tapes can be used independently or together.
This design has a robust polycarbonate casing, capable of surviving drops and knocks. It can also be recycled at the end of its useful working life.
The casing is ergonomically designed, to ﬁt the hand comfortably.
A spirit level is a logical addition to the tape measure and it compliments its functions.
It will be used by a range of trades, including builders, joiners and DIY enthusiasts.
MODEL COMPONENTS
STYROFOAM
POLYSTYRENE
DOWEL ROD RUBBER FROM
AN INNER TUBE
TRANSPARENT PERSPEX TUBE
TRANSLUCENT PERSPEX
MDF
VACUUM FORMING POLYSTYRENE
I made a model from a variety of modelling materials including:
Styrofoam Polystyrene Dowel rod Rubber MDF
Translucent perspex Translucent perspex tube
When tested, the model was found to be ‘bulky’ and relatively uncomfortable to hold. However, it was very stable,
due to its wide base. The lenses were found to be in the wrong position for proper viewing. The function buttons were easy to use and the display was in the right position for normal viewing.
The two scales, were awkward to use together, and when one was in use,
the other got in the way.
The overall design needs further development, if this is to be a successful design.
If the design is developed further, the end of life cycle disassembly of the tape measure, in readiness for recycling, will be a priority.
The lens has a RED datum line that accurately indicates the correct measurement.
The lens clearly displays both imperial and metric scales.
ERGONOMIC SHAPE
EASY TO SEE SPIRIT LEVEL
My client and other potential customers did not like this design, mainly due to its overall size.
They felt it was too large for general use, although it incorporated some good features and functions.
They suggested only one scale was necessary and that having two was more of a ‘gimmick’ than it realistic solution.
The potential clients also felt that a small spirit level was useful to those carrying
out limit DIY, but not accurate enough for professional trades people.
The shape was deemed to be less than a good ergonomic design, as it was not entirely comfortable in
the hand.
The ‘easy to see’ spirit level was referred to as ‘diﬃcult’ to see and use.
93mm
53mm
74mm
GENERAL DESCRIPTION
Robust metric and imperial, 5 metre tape measure with digital display. Its digital memory will save up to 99 measurements. The large LCD Display ensures that measurements can be read easily.
Measurements can also be read directly from the tape, through the magnifying lenses.
Other functions include; last measurement hold function and auto shut oﬀ to save battery power. Dimensions W x H x D 74 x 93 x 53mm. Tape measure length 5m. Measuring accuracy, 1 hundredth of a mm.
www.technologystudent.com © 2018 V.Ryan © 2018
https://www.facebook.com/groups/254963448192823/
https://www.facebook.com/groups/254963448192823/
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 85
PRODUCT DEVELOPMENT
SHEET 7
NAME:
RELEASE BUTTON -
when pressed the tape measure retracts. The speed of rewinding can be controlled by increasing or decreasing the pressure applied to
the button.
CONTROL RELEASE BUTTON
The smooth shape of the casing ﬁts the average hand comfortably. The shape has been designed with ergonomics in mind, allowing for easy reach of the ‘control release’ button.
The sample colour scheme is typical of tape measures. However, this design could be manufactured for the widest range of potential clients, in a variety of colours.
translucent elastomers. These materials have the combined properties of ‘plastic’ and ‘rubber’. This means that the tape measure should survive everyday knocks and blows.
The translucent casing of this design, means that the mechanism inside the casing can be seen and it adds to the aesthetics of the design.
If an LED light is added, the illumination, with the casings varied translucent colours will be visually impressive.
RUBBER GRIP
The small slot at the back of the tape measure is for a strap, for looping round a hand, or for hanging up the tape measure.
I looked at two existing tape measures, both used this system, for securing the tape to the hand during use and for hanging up, for storage.
The styrofoam model (left), shows how this type of system can be manufactured easily and initial testing would suggest that the mechanical way in which the strap is secured to the casing, needs little reﬁnement, as it is very strong.
However, some straps are manufactured from rubber or a synthetic rubber material, which is prone to wear and tear. Alternatively, a more reliable woven textile material is used.
Both of these could be replaced by using woven kevlar. This will not break and will resist most forms of extreme wear and tear.
This colour scheme incorporates the use of
STYROFOAM MODEL
When testing the two types of strap, it was found that it was virtually impossible to break the one made from the woven textile. However, the rubber / synthetic rubber strap could break with ease, if a small tear developed ﬁrst.
In a working environment, where chisels, craft knives and tools of this nature, may come in contact with the strap, rubber is not a good selection (even though it has a comfortable feel).
A further development could be to make the strap retractable, rather like the tape measure. The strap could retract into the casing, when the tape measure is in use.
CAD REPRESENTATION OF STRAP HOLDER
The scale includes both imperial and metric. The imperial scale is broken down into 1/8ths, 1/4s etc...
Potential customers could choose between, imperial, metric or a combination scale.
PLAN VIEW OF DEVELOPED TAPE MEASURE
A control release mechanism, would ensure that the tape does not rewind quickly, trapping ﬁngers. Furthermore, it would mean that the tape measure could sit on top of the materials being measured, without retracting automatically. This would making measuring long pieces much easier.
5 6 7 8
1 1 3 1 5 3 7
2 8 4 8 2 8 4 8 3
POTENTIAL
WEAK POINT
If a tear / split develops on the rubber strap, it will soon fail.
However, the overall existing design is very reliable.
TESTING OF EXISTING / SIMILAR TAPE MEASURES
www.technologystudent.com © 2018 V.Ryan © 2018
https://www.facebook.com/groups/254963448192823/
https://www.facebook.com/groups/254963448192823/
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 86
Flexible-Solar-Panel.jpg cheapsolarpanelsforsale.com
Suntrica, ﬂexible solar panel envirogadget.com
PRODUCT DEVELOPMENT
SHEET 8
NAME:
This developed idea has a combination of several improvements, from previous design pages.
The Control Release Button also has an LED. This illuminates the tape measure, until the button is
pressed retracting the tape. The LED will not be ON, when the tape is fully
retracted. The circuit controlling the LED, has a built in timer, which automatically turns oﬀ the power, after a predetermined time, conserving the battery.
A solar panel on the top grip, charges up the batteries, in the same way as a solar powered calculator works.
A ﬂexible solar panel has been added to the top grip. This technology already exists
Existing solar panel technology has been applied to the top of the tape measure, ensuring that the batteries are always recharged. Consequently, the batteries never need replacing.
A grip shown on an earlier design has been applied, which
helps the user when holding the
prevent slipping, when the tape measure is resting on the material being measured.
EXISTING FLEXIBLE SOLAR PANEL TECHNOLOGY
1 1 3 1 5 3 7 1 1 3 1 5 3 7 1 1 3 1 5 3 7 1 1 3 1 5 3 7
8 4 8 2 8 4 8 1 8 4 8 2 8 4 82 8 4 8 2 8 4 8 3 8 4 8 2 8 4 8 4
1 2 3 4 5 6 7 8 6 7 8
A scale including imperial and metric measurements has been included. This will satisfy the requirements of most potential customers.
Although the metric system dominates most industries, the imperial scale is still used.
Transparent / translucent panels, illuminated by an internal set of LEDs.
This allows the internal mechanism to be seen, adding to the designs aesthetic appeal
The kevlar strap is secured in a time tested fashion, looped around a steel / aluminium pin, held in place by the two sides of the casing.
Kevlar watch straps already exist.
A previous design has a magnifying lens, to help view the scale. This has been dropped as the tape is quite wide and the measurement is clearly seen, when the tape is in use.
I made a detailed model and carried out some initial tests, to conﬁrm that the design was worth developing further. Although not a ‘working’ model, results from the basic testing, suggested that the design had promise.
This sketch shows that developed idea, with a ﬂexible solar panel.
STYROFLEX CASING
The main material for the casing will be the elastomer, Styroﬂex because of its physical properties.
It has good tensile strength and are tear resistance. It resists chemicals and ink / paint.
It has good properties of ﬂexibility and resistance to compression.
After bending, it tends to return close to its original shape
/ form.
It can be reprocessed / recycled by raising its temperature above melting point.
Styroﬂex can be reformed during the melting process, unlike many other forms of plastics.
It can be extruded, blow moulded and injection moulded.
It can be remoulded, if the temperature is raised until the TPE becomes soft and pliable.
WOVEN KEVLAR STRAP
The casing material will need a combination of mechanical properties including; toughness, high wear resistance and a certain amount of elasticity. THERMOPLASTIC ELASTOMERS (TPE) will meet these properties.
The casing will be manufactured through either vacuum forming of injection moulding.
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018
https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018 tape measure. It also helps

## Slide 87
PRODUCT DEVELOPMENT
SHEET 9
NAME:
I have developed my clients and potential customers favourite design on this design sheet.
A dual scale has been included, showing both metric and imperial systems of measurements. The tape is quite broad allowing the scales to be read with relative ease.
A digital display has been included, allowing the user to view the measurement directly from the tape or the display. Although the display shows both metric and imperial measurements, it can be set to display the users preferred system.
The buttons control a range of features, including last measurement recall and a memory capable of storing 99 measurements.
SOLAR PANEL AND DIGITAL DISPLAY
INTEGRATED WITH STYROFLEX
TRANSLUCENT SIDE PANEL
HIGH IMPACT (HIGH DENSITY) POLYSTYRENE CASING
STYROFLEX BOTTOM GRIP WITH INTEGRATED STAINLESS STEEL STRAP PIN
DUAL SCALE
TAPE MEASURE
A disassembled version of the tape measure is below. This shows the major parts, as an exploded view.
ROCKER SWITCH WITH INTEGRATED LED
KEVLAR STRAP
The ultrabright LED light is part of the rocker
switch. When the tape is extended it
illuminates automatically. A timer circuit controls the length of time the
LED stays on. The ﬂexible solar panel recharges the internal batteries.
An improved tape end means that the tape is level when being used.
The kevlar strap is now retractable, housed inside the styroﬂex bottom grip.
A rubber bottom grip (see above), is comfortable in the hand and grips the
material it is placed on, when measuring.
The level tape, leads to a more accurate measurement being taken.
BUILT IN LED
RUBBER BOTTOM GRIP
METRIC
IMPERIAL
The high density polystyrene casings are injection moulded. Small screws hold
the two sides together, allowing them to be disassembled, for recycling after many years of use.
The tape measure is designed to be aﬀordable, tough and accurate. It is also ecologically sound,
having been carefully designed and manufactured from recyclable materials.
FUNCTION BUTTONS
THE FINAL DESIGN
My client is very happy with this design as it meets most points of the speciﬁcation. The client was consulted at every stage, especially during the development stage of the design process.
The model was extremely comfortable to hold in the hand and the switch was easy to use. This is due to the time devoted to developing the ergonomic shape/form, derived from anthropometric data.
My client liked the combined use of styroﬂex and the ﬂexible solar panel. The rechargeable batteries should never need replacing and this also applies to the ultra bright LED.
www.technologystudent.com © 2018 V.Ryan © 2018
https://www.facebook.com/groups/254963448192823/
My focus group selected the basic design from a
selection of ideas.
They were very positive
about the consideration given to the products life cycle and its end of life recycling. The use of rechargeable batteries, in combination with the solar panels, was positively received.
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 88
V.Ryan © 2012 World Association of Technology Teachers
PRODUCT DEVELOPMENT
SHEET 10
NAME:
6
1 3 1 5 3 7 3 88 44 88 22 88 44 88 4
1 1 3 1 5 3 7
4 8 2 8 4 8
7 8 6 7 8
1 1 3 1 5 3 7
1 1 3 1 5 3 7 1
8 4 8 2 8 4 8 1 8 4 8 2 8 4 82 8
1 2 3 4 5
SCALE 1:2
THIRD ANGLE PROJECTION
1
2
3
5
6
8
9
10
90 mm
88 mm
88 mm
11
24 mm
30 mm
28 mm
16mm
48 mm
20mm
KEVLAR STRAP REMOVED
10
ISOMETRIC PROJECTION
PART No | No OFF | DESCRIPTION | MATERIAL | DIMENSIONS | FINISH
1 | 1 | ROCKER SWITCH | PVC | 30x26x10mm | POLISHED
2 | 1 | ULTRA BRIGHT LED | ELECTRONIC COMPONENT | Dia.5x10xmm | N/A
3 | 1 | FLEXIBLE SOLAR PANEL | ELECTRONIC COMPONENT | 110x28x3mm | N/A
4 | 1 | LCD - DISPLAY | ELECTRONIC COMPONENT | 15x25x5mm | N/A
5 | 1 | END GRIP | ALUMINIUM | 16x8x24mm | BRUSHED
6 | 2 | CASING | POLYETHYLENE | 65x90x24mm | POLISHED
7 | 5 | FUNCTION BUTTONS | STYROFLEX | Dia.4x8mm | TEXTURED
8 | 1 | BOTTOM GRIP | SYNTHETIC RUBBER | 90x24x48mm | TEXTURED
9 | 1 | WRIST STRAP | KEVLAR | 88x26x2mm | WOVEN
10 | 2 | PAN HEAD RIVETS | ALUMINIUM | DIA3x15mm | PLANISHED
11 | 2 | TRANSLUCENT WINDOW | POLYETHYLENE | 40x35x2mm | POLISHED
65 mm
24
www.technologystudent.com © 2018 V.Ryan © 2018
https://www.facebook.com/groups/254963448192823/
https://www.facebook.com/groups/254963448192823/
7
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
www.technologystudent.com © 2018 4V.Ryan © 2018

## Slide 89
MANUFACTURE THE FINAL PROTOTYPE
HELPFUL LINKS
http://www.technologystudent.com/designpro/eg_prodlog1.html http://www.technologystudent.com/designpro/prodstate1.html
www.technologystudent.com © 2018 V.Ryan © 2018
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
https://www.facebook.com/groups/254963448192823/
IT IS GOOD PRACTICE TO KEEP A PRODUCTION LOG OF THE MANUFACTURE OF THE FINAL PROTOTYPE. THE LINKS ABOVE GIVE GUIDANCE ON THIS. MARKS ARE NOT AWARDED FOR THE PRODUCTION LOG, BUT THE PHOTOGRAPHS AND COMMENTS THAT ARE RECORDED, WILL INEVITABLY BE USEFUL WHEN WRITING THE EVALUATION.
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 90
FINAL TESTING AND EVALUATING
HELPFUL LINKS
FOLLOWING ARE THREE SLIDES OF WRITTEN ADVICE AND GUIDANCE, REGARDING EVALUATING AND TESTING A FINAL PROTOTYPE / PRODUCT.
THERE ARE THREE SLIDES SHOWING TESTING BY A CLIENT / POTENTIAL CUSTOMER
THERE ARE ALSO TWO SLIDES SHOWING POSSIBLE LAYOUTS TO A FINAL EVALUATION, WHICH IS THE STUDENT’S EVALUATION, INCLUDING HIS/HER VIEWS /OPINIONS.
REMEMBER - TO TEST THE PRODUCT AGAINST THE ORIGINAL SPECIFICATION.
www.technologystudent.com © 2018 V.Ryan © 2018
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
https://www.facebook.com/groups/254963448192823/
http://www.technologystudent.com/despro_ﬂsh/evalintegr1.html http://www.technologystudent.com/despro_ﬂsh/testeval1.html http://www.technologystudent.com/despro_ﬂsh/testeval2.html http://www.technologystudent.com/designpro/eval1.htm
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 91
AQA
AO3: Analyse and evaluate:
OCR
Evaluate (AO3)
EDEXCEL
4.1 Testing and evaluation
FINAL TESTING AND EVALUATING
HELPFUL LINKS
http://www.technologystudent.com/despro_ﬂsh/evalintegr1.html http://www.technologystudent.com/despro_ﬂsh/testeval1.html http://www.technologystudent.com/despro_ﬂsh/testeval2.html http://www.technologystudent.com/designpro/eval1.htm
www.technologystudent.com © 2018 V.Ryan © 2018
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
https://www.facebook.com/groups/254963448192823/
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 92
Designers analyse and evaluate their ﬁnished products or prototypes in order to test whether they work well and if the design can be improved.
IT IS IMPORTANT TO EVALUATE YOUR WORK CONSTANTLY DURING THE PROJECT.
Evaluation can take a variety of forms:
General discussion with other students, focus groups and the client. Questionnaires / surveys carried out at any time during the project.
Your personal views, what you think of existing designs.
Most important of all - what do you think of your designs, prototypes and ﬁnished product ?
Can you think of any other ways of evaluating your work ?
www.technologystudent.com © 2018 V.Ryan © 2018
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
https://www.facebook.com/groups/254963448192823/
https://www.facebook.com/groups/254963448192823/
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 93
What do you think of the overall design ? What changes would you make?
Are you happy with the materials you chose ? Would you make adjustments next time?
Is the colour scheme/style exactly what you expected ? What alterations would you make?
Did the project take too long to make? Would this alter the cost of manufacture?
Would it be easy to set up a production line for the manufacture of your solution?
Is your solution safe? Could it be made safer?
Are the techniques you used to make your solution adequate or would you use a diﬀerent range of manufacturing techniques?
Is the solution the right size/shape?
What are the views of other people regarding your design?
Does it work? What changes are required?
www.technologystudent.com © 2018 V.Ryan © 2018
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
https://www.facebook.com/groups/254963448192823/
CONSIDER THE FOLLOWING POINTS WHEN WRITING YOUR FINAL EVALUATION
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 94
The ﬁnal evaluation and testing is often NEGLECTED, because it is the last part to any design and make project. Do not make the mistake of completing it quickly or not doing it at all. The ﬁnal evaluation is usually relatively easy to write and is awarded signiﬁcant marks.
www.technologystudent.com © 2018 V.Ryan © 2018
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
https://www.facebook.com/groups/254963448192823/
https://www.facebook.com/groups/254963448192823/
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 95
TESTING OF FINAL DEVELOPED IDEA
SHEET 1
NAME:
1 1 3 1 5 3 7 1 8 4 8 2 8 4 8 |  |  | 1 1 3 1 5 3 72 8 4 8 2 8 4 8 |  |  | 1 1 3 1 5 3 7 3 8 4 8 2 8 4 8 |  |  |  | 1 1 3 1 5 3 7 4 8 4 8 2 8 4 8 |  |  | 
1 | 2 | 3 | 4 | 5 | 6 |  | 7 | 8 | 6 |  | 7 | 8 | 
The ﬁnal design was manufactured, as a precise model and was put through a number of tests.
They were designed to check the quality of my design/product against the speciﬁcation, agreed with
my client and other potential customers.
An ergonomics test, was one of the most important aspects of the testing and evaluation, of the ﬁnal tape measure design. It was tested in two ‘dimensions’;
A - Holding the tape, as it would normally be held for setting up for measuring. B - Holding the tape measure and operating the LED rocker switch.
A Focus Group composed of ten people were asked to test the ergonomics. Seven members found the ergonomics to be ‘very good’, three found the ergonomics to be ‘good’. Overall, I am pleased with the general ﬁndings of the focus group, as the speciﬁcation stated that good ergonomics was a priority.
GROUP MEMBER | VERY GOOD | GOOD | FAIR | POOR
1 |  |  |  | 
2 |  |  |  | 
3 |  |  |  | 
4 |  |  |  | 
5 |  |  |  | 
6 |  |  |  | 
7 |  |  |  | 
8 |  |  |  | 
9 |  |  |  | 
10 |  |  |  | 
SUMMARY | 7 | 3 | 0 | 0
LED LIGHT TEST
The circuit was tested, outside the casing, shining the LED light directly at the light meter. The LED achieves 1270 lux, providing enough light to view the scale in darkness.
A general test and a scientiﬁc test were carried out.
The tape measure was used in a shaded place, to test the illumination of the LED and the ability of a user to view the measuring scale.
A light meter was used to measure the light intensity of the ultra bright LED
All members of the focus group found the LED illumination very useful, when measuring in poor light conditions.
One suggestion was that the LED could be used as a general light source.
ULTRABRIGHT LED
employees. They used the tape on common tasks, such as preparing materials for
cutting and shaping.
Their all agreed that the tape measure had potential for future development. Four of the ﬁve workers said it was comfortable to use,
especially when held in the hand, as shown below. One suggestion was that two versions should be developed, one with an LED light and one without.
ERGONOMICS TESTING PHOTO A PHOTO B
GENERAL TESTING
The tape measure was tested by a builder and his four
SCALE - READABILITY TEST
The builders carrying out the general test, agreed that the scale was very useful, especially the imperial scale. The imperial scale has been used less and less, over the years, due to the metric system becoming dominant. When used by builders, the fact that the imperial divisions were clear and easy to read, was a plus. This meets one of my speciﬁcation requirements.
light, eﬃciently charging the batteries.
Given that the LED will not be constantly used and that the tape
measure would normally be in room level lighting conditions -
the conclusion is that this illumination system will be successful.
The environmental aspect of my speciﬁcation has been partly met.
FLEXIBLE SOLAR PANEL TEST
A sample solar panel was tested and it was shown capable of recharging the
batteries, in normal lighting conditions, in one hour.
When tested for discharge, it illuminated the LED for 10 minutes
nonstop use. The manufacturers claim that the panel collects 90% of ambient
SOLAR PANEL
WITH CIRCUIT
TM-201L LUX/FC LED LIGHT METER
I used the light sensor to ﬁnd the LED white light Luminous Intensity Measurement.
The use of an LED to illuminate the tape, helps meet the speciﬁcation requirement ‘ease of reading’ and aids accuracy.
www.technologystudent.com © 2018 V.Ryan © 2018
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
https://www.facebook.com/groups/254963448192823/
https://www.facebook.com/groups/254963448192823/
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 96
TESTING OF FINAL DEVELOPED IDEA
SHEET 2
NAME:
MATERIAL TESTING
A sample of styroﬂex was
tested using a piece of homemade equipment.
A steel tube was held
vertically, using science lab
clamps.
A ‘turned’ 100g weight was dropped down the tube and the impact damage recorded.
The styroﬂex sample had a ‘dint’, where the impact took place, but it had not cracked. Overall, very little deformity took place.
The equivalent size and thickness of a piece of HIPS High Impact Polystyrene was tested, in exactly the same way. The piece cracked from the impact area outwards and a small piece broke away at the impact point.
HARDNESS TEST
STYROFLEX
CASING
KEVLAR STRAP
TESTING KEVLAR
When testing a sample of kevlar, with a scissors, I found that it was extremely diﬃcult to cut and after a short time the scissors became blunt.
TESTING RUBBER
When testing rubber, it cut extremely easily with a scissors. Very little eﬀort was required.
Kevlar is the best choice for the strap, as it will withstand cutting, unlike the rubber which will fail, if it becomes torn or damaged in any way. Kevlar fulﬁls the material properties outlined in my speciﬁcation.
RED
YELLOW
BLUE
GREEN
30
25
20
15
10
5
COLOUR SELECTION
I showed one hundred construction students at the local college, the range of colours on oﬀer. The selection of colours was well received, with blue being the most popular.
When asked if the colour scheme was the most important factor or the operation / functions, 92 said that the tape measures operation/functions were the priority.
My speciﬁcation states that the colour scheme will be important. However, the survey suggests function before aesthetics in of greater importance.
speciﬁcation, is that the tape end grip tends to slip oﬀ the material. This usually happens, just when it is time to read the scale. An improved design was speciﬁed.
The redesigned end grip worked well when tested. In 9 out of 10 tests, the end grip remained in position whilst the tape was being used, on a typical measuring task.
The metallic tape remained straight and level when in use, allowing a more accurate measurement.
Conclusion: the Styroﬂex was the most appropriate material to select for the casing of the tape measure. Survival of knocks and drops from everyday use was more likely. Styroﬂex ﬁts the material properties outlined in my speciﬁcation.
SWING TEST
The kevlar strap of the model was put under stress, by swinging the tape measure round at speed.
Although not scientiﬁc, it is a realistic test, as this may happen during its lifetime. The strap survived and showed no sign of fatigue. This was repeated ﬁfty times.
END GRIP
0.00v
CONDUCTIVITY TEST
I carried out a simple conductivity test on a sample of casing material (styroﬂex).
The meter showed that it did not conduct current at all, making it an
excellent insulator. Although the low voltage batteries do not carry a direct health and safety risk, the styroﬂex, will prevent an accidental short circuit, which is a potential ﬁre hazzard.
END GRIP TESTA standard problem emphasised in the
92mm
www.technologystudent.com © 2018 V.Ryan © 2018
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
https://www.facebook.com/groups/254963448192823/
TAPE EXTENSION TEST
The tape was extended stage by stage and a weight of 50 grammes attached.
The tape stayed level until it was extended by 92mm, it then lost its shape.
The focus group agreed that this was acceptable, as most tapes they had used, failed even at a light touch. This fulﬁls a speciﬁcation requirement.
Tape extension is very important as a ‘weak’ tape, that loses its shape, leads to a loss in accuracy and infuriates the user. The speciﬁcation refers to this aspect of the design being important.
www.technologystudent.com © 2018
https://www.facebook.com/groups/254963448192823/
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
V.Ryan © 2018

## Slide 97
PRODUCT TESTING
PHOTOGRAPH OF TESTING
FINDINGS OF THREE TESTERS
DESCRIPTION OF TESTING
My electronic / mechanical childrens toy was tested for a week in a school nursery. It was used every school day and still worked at the end of the time period.
The children were taught how to use the ‘maze’ game, especially how the handles operated. They were not shown how to replace the batteries as this was regarded as being unsafe.
The rechargeable batteries are small and should be replaced by an adult. The life span of the batteries was recorded.
The game was deliberately dropped twice to check its robustness and survivability. It was checked for splinters and small pieces breaking away (these would be a hazard for young children).
PERSON 1: TEACHING ASSISTANT (SUPERVISING)
As expected it got some rough handling and was dropped once or twice. The batteries had to be replaced. This was difficult as a screwdriver was required. This could be regarded as a safety feature, to prevent young children opening the circuit compartment, but it was still inconvenient.
The children enjoyed the game and some continuously played with it. The game is slightly addictive, for some young children.
Overall, it is a good game, worthy of further development.
PERSON 2: STATEMENTS FOR ONE YOUNG CHILD
Did you enjoy the game?
Yes.
How long did you play the game for?
30 minutes.
Did your friends like the game? Some liked it. Some found it a little boring after a while.
Would you play the game again?
Yes.
PERSON 3: ADULT TESTER
I found the handles for moving the mechanical parts of the game a possible weak point. With force, they may break away. A small handle could be sallowed by a very young child.
The circuit worked well and without a screwdriver, it is impossible to open the circuit and battery compartment. This is a good safety feature as it stops young children damaging the circuit or taking out the small batteries.
I saw children enjoying the game.
Young children should play this game only when supervised.
in
90 100 110
5 6 7 8 9 4 1 2 3 4 5 6
1 2 3 4 5 6 7 8 91 1 2 3 4 5 6 7 8 9 2 1 2 3 4 5 6 7 8 93 1 2 3 4 7 8 95 1 2 3 4 5 6 7 8 96
By V.Ryan
0
OFF ON ZERO
INCH/MM
80.00
10 20 30 40 50 60 70 80 mm 120 130 140 150 mm
MECHANICAL / ELECTRONIC GAME UNDERGOING TOLERANCE TESTING.
THE MEASUREMENTS ARE BEING CHECKED TO ENSURE THAT THEY ARE THE SAME AS ON THE WORKING DRAWING
www.technologystudent.com © 2018 V.Ryan © 2018
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
https://www.facebook.com/groups/254963448192823/
https://www.facebook.com/groups/254963448192823/
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 98
My Product Specification is written below. It is a check list that will help me develop my product.
It has been checked and agreed with my client / customer
MY EVALUATION AGAINST THE SPECIFICATION
PRODUCT: EASY CHAIR WRITING REST
EVALUATION AGAINST EACH SPECIFICATION POINT
SPECIFICATION POINT
POTENTIAL CUSTOMERS: The ‘writing rest’ must be useful and appeal to a wide range of potential customers.
FUNCTIONS - EASE OF USE: The
‘writing rest’ must allow the user to write
and read comfortably, whilst sat in an easy
chair.
FUNCTIONS - LIGHTING: The ‘writing
rest’ should have an integrated light source.
LIGHTWEIGHT: The writing rest should be
lightweight.
ADJUSTABLE: The writing rest should be adjustable, allowing individuals to set it up to suit their seating position.
www.technologystudent.com © 2018 V.Ryan © 2018
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
https://www.facebook.com/groups/254963448192823/

## Slide 99
SPECIFICATION POINT
ERGONOMICS: The ‘writing rest’ must be suitable for use with a wide range of easy chairs, and by the widest possible range of potential customers.
ERGONOMICS: The light should be
adjustable, so that it can be focussed on the
page being read by the user.
SAFETY: The product must be safe to use, even when being adjusted.
LIFE CYCLE AND SUSTAINABILITY: The
writing rest will be manufactured from sustainable materials such as recycled and
reclaimed materials (aluminium, natural woods
and recyclable plastics, including polypropylene). Also, the materials will be reclaimed at the end of it’s useful working life.
A E S T H E T I C A P P E A R A N C E ( S H A P E ,
COLOUR, TEXTURE): The writing rest will be designed in a ‘Bauhaus’ style, as preferred by my main client.
EVALUATION AGAINST EACH SPECIFICATION POINT
www.technologystudent.com © 2018 V.Ryan © 2018
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
https://www.facebook.com/groups/254963448192823/

## Slide 100
MY EVALUATION
PRODUCT PHOTOGRAPHS
POSITIVE POINTS
I like the overall design of my project. It is a suitable game for a young child as it helps in the development of hand/eye coordination. The game and its container are safe as the edges are not sharp and there are no small pieces that could be swallowed.
The joints are accurate and hold the sides together permanently. The wood is pine and this is quite cheap to buy and yet strong and able to withstand everyday knocks.
I like the colour scheme as it reflects the results of my questionnaire. The perspex lid is red as this was found to be the favourite of children aged 5 to 9 years of age.
The lid closes quite smoothly and the b u tte r fl y h i n g e s w o r k w e l l . Th e translucent lid allows the internal maze to be seen and the pattern looks quite interesting.
I like the position of the coat of arms. This has been machined on a CNC machine.
Overall the game works well. The maze is complex but with effort it can be beaten.
HANDLE
COAT OF ARMS
LID
IMPROVEMENTS
Although I like my maze game it could be improved and be even better:
A selection of woods could be available so that parents could choose the type they like best. A wood such as mahogany would increase the price but I think parents would be prepared to pay a higher price for a quality product.
A selection of handle shapes would allow the user to choose the shape they like best. The game could be supplied with a variety of shapes making the game more interesting to look at and play.
Customers could select lids from a range of colours including translucent and transparent perspex.
The coat of arms could be chosen by the customer to reflect the family name. This would personalise the product and lift the price of sale.
In future the maze game could be based on a rectangular, circular or even triangular shape.
www.technologystudent.com © 2018 V.Ryan © 2018
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
https://www.facebook.com/groups/254963448192823/
https://www.facebook.com/groups/254963448192823/
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 101
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018
www.technologystudent.com provides all your needs for the delivery of the New Design and Technology GCSE. Free to access - but please respect the copyright
IMPORTANT LINKS - FOR A SUCCESSFUL DELIVERY OF THE COURSE
ITERATIVE DESIGN AND THE NEA
http://www.technologystudent.com/designpro/despro1.htm
DETAILED CONTENT AND EXERCISES THAT FOLLOW THE GCSE SPECIFICATION
http://www.technologystudent.com/despro_ﬂsh/new_maths1.html DESIGNERS, DESIGN MOVEMENTS AND COMPANIES
http://www.technologystudent.com/despro_ﬂsh/Designer1.html MATERIALS, EQUIPMENT AND INDUSTRIAL PROCESSES
http://www.technologystudent.com/despro_ﬂsh/materials_main1.html http://www.technologystudent.com/equip1/equipex1.htm
GRAPHICS, DRAWING TECHNIQUES AND INDUSTRIAL PROCESSES
http://www.technologystudent.com/despro_ﬂsh/graphics_main1.html MATHEMATICS AND DESIGN AND TECHNOLOGY
http://www.technologystudent.com/despro_ﬂsh/new_maths1.html TOTAL REVISION - FOR EXAMINATIONS
http://www.technologystudent.com/despro_ﬂsh/new_revison1.html http://www.technologystudent.com/despro_ﬂsh/vid_channel2.html