## Slide 1: FERROUS METALS
NAME | ALLOY OF | PROPERTIES | USES
Mild Steel | Carbon 0.1 - 0.3% Iron 99.9 - 99.7% | Tough. High tensile strength. Can be case hardened. Rusts very easily. | 
Carbon Steel | Carbon 0.6 - 1.4% Iron 99.4 - 98.6% | Tough. Can be hardened and tempered. | 
Stainless steel | Iron, nickel and chromium. | Tough, resistant to rust and stains. | 
Cast iron | Carbon 2 - 6% Iron 98 - 94% | Strong but brittle. Compressive strength very high. | 
Wrought iron | Almost 100% iron | Fibrous, tough, ductile, resistant to rusting. | 
NAME | COLOUR | ALLOY OF; | PROPERTIES | USES
Aluminium | Light grey | Aluminium 95% Copper 4% Manganese 1% | Ductile, soft, malleable, machines well. Very light. | 
Copper | Reddish brown | Not an alloy | Ductile, can be beaten into shape. Conducts electricity and heat. | 
Brass | Yellow | Mixture of copper and zinc 65% - 35% most common ratio. | Hard. Casts and machines well. Surface tarnishes. Conducts electricity. | 
Silver | Whitish grey | Mainly silver but alloyed with copper to give sterling silver. | Ductile, Malleable, solders, resists corrosion. | 
Lead | Bluish grey | Not an alloy. | Soft, heavy, ductile, loses its shape under pressure. | 
NON-FERROUS METALS
Complete the ‘USES’ section of the two tables below.
HELPFUL LINK: https://www.technologystudent.com/designpro/metals1.htm
V.Ryan © 2008 World Association of Technology Teachers