## Slide 1: Level 1/Level 2 GCSE (9–1)
Candidate Name | Centre Number |  |  |  |  | Candidate Number |  |  |  | 
COMPONENT 1
TIME ALLOWED - 1 hour 45 minutes
DESIGN AND TECHNOLOGY - GCSE SAMPLE PAPER 1
EQUIPMENT REQUIRED
Drawing and writing equipment, coloured pencils and a calculator
INSTRUCTIONS
You are to answer all questions.
This example examination paper can be duplicated and printed out if required but not edited in any way.
The links to www.technologystudent.com cannot be removed.
The PDF ﬁle can be stored on school / college systems and distributed electronically (NO EDITING ALLOWED)
PLEASE RESPECT THE COPYRIGHT - report infringers to techteacher@technologystudent.com Not be distributed at courses or by course instructors / consultants
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 2
Section A - CORE
Answer all the questions in this section
1a. Materials are selected for the manufacture of products, usually because they exhibit suitable properties.
Complete the table below by adding a description and explain the material’s properties.
The ﬁrst answer has been completed as an example of the layout of the table.
PRODUCT DESCRIPTION PROPERTY
WORLD ASSOCIATION OF TECHNOLOGY T |  | PEWTER CASTING JELLEWERY EACHERS https://www.facebook.com/groups/2549634481928 | Pewter can be cast by at low temperatures, forming detailed shapes. 23/ www.technologystudent.com © 2018 V.Ryan © 2018 | 
 | HELPFUL LINK | http://www.technologystudent.co | m/rmﬂsh1/pine2.html | 
 |  | PINE WOOD - LAMP | 1 mark | 
 | HELPFUL LINK | http://www.technologystudent.co | m/joints/pet1.html | 
 |  | FOOD TRAY POLYETHYLENE TEREPHTHALATE | 1 mark | 

## Slide 3
PRODUCT
DESCRIPTION
PROPERTY
 | HELPFUL LINK ht |  | tp://www.technologystudent.co | m/joints/nonferrous1.html |  | 
WORLD ASSOCIATION OF TECHNOLOGY |  |  | ALUMINIUM DRINKS CAN TEACHERS https://www.facebook.com/groups/2549634481928 | 1 mark 23/ www.technologystudent.com © 2018 V.Ryan © 2018 |  | 
 |  | HELPFUL LINK | http://www.technologystudent.c | om/despro2/prneﬀ2.htm |  | 
inSIGHT |  |  | POSTER UV VARNISHED QUALITY PAPER | 1 mark |  | 
 |  | HELPFUL LINK | http://www.technologystudent.c | om/joints_ﬂsh/nylon1.html |  | 
 |  |  | NYLON WATERPROOF CLOTHING | 1 mark |  | 

## Slide 4
HELPFUL LINK http://www.technologystudent.com/despro_ﬂsh/revise9.html
(I) How could thermochromic inks, applied to the label, improve the presentation of the can? 2 marks
LABEL TO BE PLACED HERE
(II) The manufacturers of the aluminium can intend to operate a close loop recycling system. What is this? 2 marks
HELPFUL LINK http://www.technologystudent.com/prddes1/closeloop1.html
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/ www.technologystudent.com © 2018 V.Ryan © 2018
1b. The manufacturer of the can, intend to use a label with thermochromic inks.

## Slide 5
2a. Name a suitable material for the manufacture of this chair? In your answer explain the physical properties that make it suitable. 2 marks
HELPFUL LINK http://www.technologystudent.com/rmﬂsh1/alevq2.html
https://www.facebook.com/groups/254963448192823/
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
www.technologystudent.com © 2017 V.Ryan © 2017
2d. A scaled model of the chair has been manufactured and placed in a ‘model’ room. It stands inside the circle shown below. Calculate the area of the circle.
Include your working out and formula. 3 marks
The circle has a radius of 100mm. What is the area of the circle?
Radius 100mm
HELPFUL LINK http://www.technologystudent.com/pdf14/maths4.pdf Page 2
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/ www.technologystudent.com © 2018 V.Ryan © 2018
2. The photograph shows a modernist ‘plastic’ chair.

## Slide 6
HELPFUL LINK http://www.technologystudent.com/joints/pet1.html
2c. The modernist chair will be supplied with a textile cover manufactured from polyester. List two advantages of using polyester. 2 marks
(i)
(ii)
2d. The chair is to be manufactured on a production line. What is a production line?
2 marks
HELPFUL LINK http://www.technologystudent.com/prddes1/prodline1.html
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 7
3a. The diagram below represents a type of force.
(I) Name the force.
1 mark
(I) Describe the force. 1 mark
HELPFUL LINK http://www.technologystudent.com/forcmom/force1.htm
3b. In terms of ‘moments of force, what is a state of equilibrium? 2 marks
HELPFUL LINK http://www.technologystudent.com/forcmom/force2.htm
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 8
3c. The diagram below shows a state of equilibrium. Using the formula below, prove that a state of equilibrium exists. 3 marks
HELPFUL LINK http://www.technologystudent.com/forcmom/force2.htm
FORMULA: CLOCKWISE MOMENTS = ANTI-CLOCKWISE MOMENTS
3d. Companies manufacturing cars often work with a system called ‘Lean Manufacturing’. What is Lean Manufacturing? 4 marks
HELPFUL LINK http://www.technologystudent.com/despro_3/lean2.html
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 9
4a. The object shown opposite is seen in many mechanical devices. What is its name?
1 mark
HELPFUL LINK http://www.technologystudent.com/gears1/gears1.htm
A
60 TEETH
B
30 TEETH
DRIVER (EFFORT)
DRIVEN (LOAD)
HELPFUL LINK http://www.technologystudent.com/gears1/gears5.htm
4b. Calculate the Velocity Ratio (Gear Ratio) for the spur gears seen opposite. Include your working out. 4 marks
4c. Opposite is an example of one way of illustrating a graph.
What is this style of graph called?
1 mark
HELPFUL LINK http://www.technologystudent.com/designpro/quest1.htm
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 10
WIND FARM
4
: SOLAR POWER
: 0.5
EXPLANATION:
The question is about alternative energy.
4d. A local wind farm produces 4 terawatt hours of electricity over a year. At the same time, a solar farm produced 0.5 terawatt hours of electrical power. What is the ratio - Wind farm : Solar Power ? 3 marks
HELPFUL LINK http://www.technologystudent.com/pdf14/ratios1.pdf Page 12
4e. Write three advantages of using wind power to produce electricity.
3 marks
HELPFUL LINK http://www.technologystudent.com/energy1/wind8.htm
www.technologystudent.com © 2017
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
V.Ryan © 2017
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 11
200mm
150mm
60mm 55mm |  | 
50mm |  | 
CREASES
5. The Illustrations show a solution for an aluminium remote control organiser.
HELPFUL LINK http://www.technologystudent.com/rmﬂsh1/remote16.html
SECTION B – METALS
Answer ALL questions
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 12
5a. The remote control organiser needs to be improved to include the following speciﬁcation points.
The remote controller must:
Have a base that adds stability.
  Be interlockable / stackable with other units of the same design.
(iii) The unit must be easy to pick up, with all the remotes in place.
Use notes and/or sketches to show how the remote control holder could be modiﬁed to satisfy the addition speciﬁcation points, listed above.
Produce clear drawings / sketches, using the outline of the original design to show how a base can be added and the other speciﬁcation points met.
6 marks
HELPFUL LINK http://www.technologystudent.com/rmﬂsh1/remote16.html
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 13
HELPFUL LINKS http://www.technologystudent.com/rmﬂsh1/remote16.html http://www.technologystudent.com/joints_ﬂsh/metal2.html
5b. The aluminium remote organiser must be available in a range of durable colours as shown below. This is achieved through an anodised ﬁnish.
SAMPLE ANODISED COLOUR FINISHES
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/ www.technologystudent.com © 2018 V.Ryan © 2018
In the space below explain / describe the anodising process. 4 marks

## Slide 14
HELPFUL LINK http://www.technologystudent.com/joints/mater2.html
6a. Carefully study the ‘Thermo-cup’. This type of cup keeps a hot drink warm for a reasonable amount of time. The lid helps prevent spillage.
The container is manufactured from stainless steel.
Write two reasons why stainless steel is a suitable material for the container.
4 marks
(I)
(II)
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 15
HELPFUL LINK http://www.technologystudent.com/equip1/heat2.htm
6b. The pliers seen opposite has case hardened jaws.
Use notes and/or sketches to explain/describe the process of hardening and tempering.
Use clear sketches and notes in your answer.
4 marks
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 16
HELPFUL LINK http://www.technologystudent.com/designpro/ergo1.htm
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
https://www.facebook.com/groups/254963448192823/ www.technologystudent.com © 2018 V.Ryan © 2018
6c. The handles / levers of the pliers have been ergonomically designed to ﬁt the hand, using anthropometric data.
What is anthopometrics ?
2 marks

## Slide 17
HELPFUL LINK http://www.technologystudent.com/joints/mater2.html
6d. The ‘container’ of the thermo-cup is mass manufactured from stainless steel sheet. In the space below, explain the manufacturing process. Use both notes and sketches. 6 marks
The container is manufactured from stainless steel.
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 18
SIDE (ALUMINIUM)
STRENGTHENING PIECE (STEEL)
SHELF (SHEET STEEL)
HANDLE (STEEL)
7. The diagram opposite shows a folding trolley. The handle can be adjusted to diﬀerent heights and the steel shelf folds upright.
7a. Why is tube the most suitable section to be used in the manufacture of the trolley? 4 marks
HELPFUL LINK http://www.technologystudent.com/despro_3/metrolly1.html
7b. Why has small diameter of steel rod been used as a strengthening piece?
1 mark
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 19
7c. A student measures the dimensions (measurements) for the ‘round section’ handle of a machine vice, that he intends to manufacture. The student measures the radius of an existing handle and ﬁnds it to be 25mm.
What is the circumference of the handle? What is the area of the end of the handle?
3 marks
2 marks
AREA = πr ²
π (pi) = 3.14
FORMULA
CIRCUMFERENCE = 2 x π x r
π (pi) = 3.14
FORMULA
www.technologystudent.com © 2017
https://www.facebook.com/groups/254963448192823/
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
V.Ryan © 2017
HELPFUL LINK http://www.technologystudent.com/pdf14/maths4.pdf Page 11
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 20
SHEET STEEL
SIDE (ALUMINIUM)
STRENGTHENING PIECE (STEEL)
SHELF (SHEET STEEL)
SHEET STEEL
SHEET STEEL
An hydraulic press is used to press shapes into sheet steel and also to cut out shapes. This is how the ‘shelf’ has been manufactured.
7d. The incomplete stages, showing/describing the manufacture of the sheet steel part, are outlined below.
Complete the notes and drawings. Add all the missing parts. 2 marks per stage (6 marks in total)
HELPFUL LINK http://www.technologystudent.com/despro_3/hydaul1.html
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
HANDLE (STEEL)
https://www.facebook.com/groups/254963448192823/ www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 21
8. The table shown below, has been manufactured from gilded metal and has a lacquered ﬁnish.
8a. Gilded metal is metal, that has been coated with a more precious metal, such as bronze or even silver and gold. Why has clear lacquer been applied as a ﬁnish?
2 marks
HELPFUL LINK http://www.technologystudent.com/joints_ﬂsh/metal7.html
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 22
8b. The process called ‘electroplating’ has been used to applied a coating of the expensive metal to the cheaper base metal. What is electroplating? Use both notes and a sketch(s) in your answer.
7 marks
HELPFUL LINK http://www.technologystudent.com/joints_ﬂsh/metal8.html
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 23
FERROUS METALS |  | 
NON-FERROUS METALS |  | 
8c. Complete the table of ferrous and non-ferrous metals by adding two examples of each. 4 marks
FERROUS METALS - Metals that contain iron.
NON-FERROUS METALS - Metals that do not contain iron.
HELPFUL LINK http://www.technologystudent.com/joints/ferous1.html
8d. Either a FERROUS or NON-FERROUS metal from your completed table. Describe a suitable practical application for your chosen metal and explain why each is suitable. Total of 5 marks
METAL:
PRACTICAL APPLICATION:
(1 mark)
WHY SUITABLE:
(4marks)
http://www.technologystudent.com/joints/ferous1.html HELPFUL LINKS http://www.technologystudent.com/joints/fermetal1.html
http://www.technologystudent.com/joints/nonferrous1.html
www.technologystudent.com © 2018
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
V.Ryan © 2018

## Slide 24
SECTION B – PAPER AND BOARDS
Answer ALL questions
5. A design solution for a Charity Collection Box, for a charity called ‘Be Active’ is shown below. The charity aims to promote active life styles to all age groups.
100 % recycleable
Lightweight
Environmentally friendly material.
Materials supplied from a certiﬁed sustainable source.
Supplied in ﬂat sheet form and folded to form the 3D version, when required .
CUT
CUT
CUT
CUT
TAB
TAB
CUT SLOT
CUT SLOT
FOLD
FOLD
FOLD
FOLD
FOLD
FOLD
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 25
5a. The charity collection box for the charity ‘Be Active’, needs to be improved to include the following speciﬁcation points.
The charity collection box must:
(I) Have an appealing logo applied to the back, that reﬂects ‘be active’.
(I) Appeal to all age groups.
(iii) The unit must be easy to pick up and must have a simple handle.
Use notes and/or sketches to show how the collection box could be modiﬁed to satisfy the addition speciﬁcation points, listed above
Produce clear drawings / sketches, using the outline of the original design to show how the additional speciﬁcation points can be met.
6 marks
BACK
HELPFUL LINK http://www.technologystudent.com/despro_ﬂsh/graphics_charity.html
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 26
Explain why the materials identiﬁed on the diagram, are suitable for the packaging.
4 marks
MATERIAL: EXPLANATION:
MATERIAL:
EXPLANATION:
HELPFUL LINKS http://www.technologystudent.com/prddes1/perfpk3.html http://www.technologystudent.com/prddes1/perfpk13.html
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/ www.technologystudent.com © 2018
5b. The drawing below shows the packaging for perfumed products.
V.Ryan © 2018

## Slide 27
6a. The free car park sign has been produced by the Design and Technology Department of a school, for an Open Evening.
HELPFUL LINK http://www.technologystudent.com/despro_3/vinylquest1.html
6b. Drinks cartons such as those manufactured by Tetra Pak, are manufactured from laminated card. Why is this? 2 marks
HELPFUL LINK http://www.technologystudent.com/despro_ﬂsh/laminate1.html
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/ www.technologystudent.com © 2018 V.Ryan © 2018
Explain why a vinyl cutter is the most appropriate way of cutting the ‘vinyl lettering’.
2 marks

## Slide 28
HELPFUL LINK http://www.technologystudent.com/despro_ﬂsh/charity9.html
6c. The corrugated card charity collection box shown opposite, is manufactured from recycled card, processed into Corrugated card.
Corrugated board is supplied in diﬀerent thicknesses.
On the diagram below, 4 thicknesses of corrugated card are shown. One has been labelled for you.
Add labels to the other three thicknesses.
3 marks
SINGLE FACE
6d. Corrugated board can be recycled. In the space opposite, draw / sketch the recycling symbol that applies to corrugated board.
1 mark
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 29
HELPFUL LINKS http://www.technologystudent.com/grp08/prnt1.html http://www.technologystudent.com/designpro/prtpro5.htm
6e. The graphics / colour and decoration is to be added to the packaging for perfumed products (question 5b). In the space below, name a suitable printing process, draw a labelled diagram to represent the process and add notes that explain the process.
Total of 8 marks
PROCESS NAME:
(1 mark)
LABELLED DIAGRAM
(4 marks)
NOTES: (3 marks)
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 30
HELPFUL LINK http://www.technologystudent.com/despro_ﬂsh/foilblk1.html
LETTERING TO BE FOIL BLOCKED
6f. The design team working on the packaging for a perfumed product, have decided to add the name of the product (in gold / silver lettering) through ‘Foil Blocking’. In the space below, explain the foil blocking process. Use notes and sketches in your answer.
Total of 5 marks
LABELLED SKETCH ( 3 marks)
NOTES (2 marks):
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 31
https://www.facebook.com/groups/254963448192823/
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
www.technologystudent.com © 2017 V.Ryan © 2017
400mm
200mm
500mm
A new lid has been designed for the packaging (see below). The packaging has been redesigned to suit this shape.
7a. Calculate the area of the material required for the lid, before it is cut to shape (the overall rectangle of material required, before it is cut to an L shape). 2 marks
7b. Calculate the area of the ﬁnal L shaped lid.
3 marks
250mm
HELPFUL LINK http://www.technologystudent.com/pdf14/maths3.pdf Page 6
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 32
8a. Manufacturers of the packaging are encouraged to source their materials from sustainable forests.
What is a sustainable forest and why are sustainable forests important? 3marks
http://www.technologystudent.com/prddes1/susenv1.html http://www.technologystudent.com/joints/sustain1.html
HELPFUL LINKS
8b. The logo shown opposite is sometimes printed on timber and packaging.
Explain the meaning of this logo. 3 marks
HELPFUL LINK http://www.technologystudent.com/joints/sustain1.html
https://www.facebook.com/groups/254963448192823/
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 33
8c. A clear window has been added to the packaging for a perfumed product.
List one advantage of adding a window and one disadvantage. 2 marks
ADVANTAGE:
DISADVANTAGE:
HELPFUL LINK http://www.technologystudent.com/prddes1/perfpk5.html
8d. The clear window is manufactured from BIOPOL. Describe / explain three reasons why this material is a good choice. 3 marks
http://www.technologystudent.com/prddes1/biopola.html http://www.technologystudent.com/prddes1/biopol3.html
HELPFUL LINKS
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 34
8e. In the space below, sketch a labelled diagram that represents the life cycle of Biopol.
4 marks
http://www.technologystudent.com/prddes1/biopola.html http://www.technologystudent.com/prddes1/biopol3.html
HELPFUL LINKS
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 35
9a. Packaging has a variety of functions. Complete the table below by stating a function, followed by an explanation. The ﬁrst row has been completed for you. Total of 9 marks
HELPFUL LINK http://www.technologystudent.com/despro2/packfn1.htm
FUNCTION | EXPLANATION
To protect a product from damage or contamination by micro-organisms and air, moisture and toxins. | Protected against being dropped, crushed, and the vibration it suﬀers during transport. Delicate products such as fruits need to be protected by a rigid package such as a laminated container. It must also be protected against micro-organisms, chemicals, soil and insects.
1 mark | 2 marks
1 mark | 2 marks
1 mark | 2 marks
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 36
Manufactured from a food safe material. Free from chemicals such as BPA, PVC and Phthalates.
Clips hold the lid tightly shut and contents sealed in. Secure food storage.
Drop resistant, relatively unbreakable.
Integrated drinks container Separate food compartments.
Personalised photographic lid, simple logo/symbol.
Recycling and Healthy Eating symbols.
CLIPS
TYPICAL FOOD CARRIER
INTEGRATED
DRINKS COMPARTMENTS CONTAINER
PERSONALISED FRONT/LID
www.technologystudent.com © 2018
SECTION B – POLYMERS
Answer ALL questions
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
V.Ryan © 2018

## Slide 37
5a. The Food Carrier, needs to be improved to include the following speciﬁcation points.
The food carrier must:
(I) Have an ergonomically designed handle.
(I) Have an area that includes a logo, representing healthy eating.
(iii) The drinks container must be detachable, so that it can be used separately.
Use notes and/or sketches to show how the food carrier could be modiﬁed to satisfy the addition speciﬁcation points, listed above
Produce clear drawings / sketches, using the outline of the original design to show how the additional speciﬁcation points can be met.
6 marks
HELPFUL LINKS
http://www.technologystudent.com/prddes_2/carrier14.html http://www.technologystudent.com/prddes_2/carrier6.html http://www.technologystudent.com/prddes_2/carrier1.html
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 38
5b. Name a suitable material for the manufacture of the food carrier.
1 mark
HELPFUL LINK http://www.technologystudent.com/prddes_2/carrier6.html
5c. The food carrier is manufactured through a process called Blow Moulding. Describe blow moulding. 3 marks
HELPFUL LINK http://www.technologystudent.com/prddes_2/carrier20.html
5d. In the space below, draw a labelled diagram that represents the Blow Moulding process. 4 marks
HELPFUL LINK http://www.technologystudent.com/prddes_2/carrier20.html
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 39
5e. Why is the material you named in question 5b, suitable for the manufacture of this food carrying product. 2 marks
HELPFUL LINK http://www.technologystudent.com/prddes1/lunch5.html
HELPFUL LINK http://www.technologystudent.com/prddes1/lunch5.html
5f. Name another material that would be suitable for the food carrier and explain why it is suitable. 2 marks
NAME:
WHY SUITABLE:
HELPFUL LINK http://www.technologystudent.com/prddes_2/carrier6.html
5g. in the space opposite, sketch the recycling symbol for material you named in question 5b. 2 marks
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 40
6a. The lunch carrier has proved popular with young children, because it comes with the free gift of a model glider. The parts of the glider push out of a polystyrene sheet and ﬁt together.
Name and describe the industrial process that is capable of producing the free gift.
You must include notes and a sketch(s) in your answer.
6 marks
SKETCH
NOTES ( Marks) :
PROCESS NAME:
(1 Mark)
HELPFUL LINK http://www.technologystudent.com/rmprp07/glidr2.html
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 41
7a. The products seen below are manufactured from oxo-degradable polymers
(i) What are Oxo-degradable Polymers?
1 mark
HELPFUL LINK http://www.technologystudent.com/joints_ﬂsh/oxodegrad1.html
(ii) Although oxo-degradable polymers decay over several months, when buried in soil, they are derived from crude oil. What is it that allows them to decay?
2 marks
(iii) Describe two products that are often manufactured from oxo-degradable polymers.
2 marks
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 42
HEIGHT = 120mm
R= 60mm
8a. An engineering company has manufactured a ‘plastic / polymer’ cylinder. This is for a company that will machine the part for the automotive industry.
What is the volume of the cylinder?
5 marks
FORMULA
v = πr ²h
volume = pi x radius² x height
π (pi) = 3.14
HELPFUL LINK http://www.technologystudent.com/pdf14/maths_cylinder1.pdf Page 3
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 43
Write two reasons why this material is suitable for the food container.
Total of 4 marks
(i)
(ii)
HELPFUL LINK http://www.technologystudent.com/joints/pet1.html
(iii) List two other products that are manufactured from polyethylene terephthalate.
2 marks
(iv) Name and describe the process used to manufacture the food container.
2 marks
HELPFUL LINK http://www.technologystudent.com/joints/petevac1.html
www.technologystudent.com © 2018
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
9a. The food container seen opposite, is manufactured from polyethylene terephthalate, pet, pete, (polyester).
V.Ryan © 2018

## Slide 44
HELPFUL LINK http://www.technologystudent.com/joints/petevac1.html
9b. Produce a labelled sketch(s) that represents the manufacturing process you named and describe in the previous question (5k (iv)) 3 marks
9c. The food container undergoes Quality Control and Quality Assurance during the manufacturing process. What is the diﬀerence between Quality Control and Quality Assurance? 4marks
HELPFUL LINK http://www.technologystudent.com/prddes1/quality1.html
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 45
10. Describe how ‘polymers’ can signiﬁcantly contribute to the sustainability of our use of materials. 9 marks
http://www.technologystudent.com/joints_ﬂsh/oxodegrad1.html http://www.technologystudent.com/joints/pla1.html
HELPFUL LINKS http://www.technologystudent.com/prddes1/closeloop1.html
http://www.technologystudent.com/prddes1/closeloop2.html http://www.technologystudent.com/despro_ﬂsh/morals2.pdf Page 5 onwards
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 46
An engineer has designed a barrier system for a roller coaster. The specification drawn up by the client says - “As a carriage approaches the platform, it breaks a light beam and the barrier is lowered, stopping excited and unruly riders getting too close to the stopping carriages.
The engineer has decided to use a PIC microcontroller, to control the motor that raises and lowers the barrier. The student uses outputs 1 and 2 to control the motor. Output 1 will turn the motor on and off. Output 2 changes the direction of the motor.
LIGHT SENSOR
RYAN RAIL SYSTEMS
 | RL |  |  | 
OUTPUT 1
OUTPUT 2
0v
M
16 15 14 13 12 11 10 9
1 2 3 4 5 6 7 8
ULN2803
OUTPUTS
Q7 Q6 Q5 Q4 Q3 Q2 Q1 Q0
- +
18 17 16 15 14 13 12 11 10
GENIE E18
1 2 3 4 5 6 7 8 9
A/D 0 A/D 1 A/D 2 D6 D7
INPUTS
SECTION B – SYSTEMS
Answer ALL questions
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 47
5a. The circuit, needs to be improved to include the following speciﬁcation points.
The circuit must:
(I) The relay must have diode protection.
(I) The motor must lift and lower the barrier.
(iii) The circuit must have a simple on/oﬀ switch, that can be used in event of an accident / emergency situation.
Use notes and/or sketches to show how the circuit could be modiﬁed to satisfy the addition speciﬁcation points, listed above
Produce clear drawings / sketches, using the outline of the original design to show how the additional speciﬁcation points can be met.
6 marks
HELPFUL LINKS
 | RL |  |  | 
OUTPUT 1
OUTPUT 2
0v
M
http://www.technologystudent.com/sysprp7/sysq08a.html http://www.technologystudent.com/sysprp08/quest5.html
https://www.facebook.com/groups/254963448192823/
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 48
IMPURITIES
SILICON
+
_
0.06
FREE ELECTRONS
SUNLIGHT
5b. Photovoltaics is a form of solar power. Explain, in simple terms, how a photovoltaic panel works. 2 marks
HELPFUL LINK http://www.technologystudent.com/energy1/solar5.htm
HELPFUL LINK http://www.technologystudent.com/energy1/solar6.htm
5c. Describe two practical applications of solar power. 2 marks
www.technologystudent.com © 2018
https://www.facebook.com/groups/254963448192823/
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
V.Ryan © 2018

## Slide 49
6a. The breadboard shown opposite is used to test circuits. Describe one advantage of using a breadboard. 2 marks
HELPFUL LINK http://www.technologystudent.com/elec1/bread1.htm
6b. Software can be used to design a circuit and then to simulate the circuit working. What are the advantages of using software to simulate circuits in operation? 2 marks
HELPFUL LINK http://www.technologystudent.com/pics/picgen1.html
https://www.facebook.com/groups/254963448192823/
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 50
The product seen opposite, is a warning light system, composed of a ‘plastic’ casing and an electronic circuit.
When the switch is ‘on’, the LEDs ﬂash.
6c. What thermoplastic material, is most suitable for the manufacture of the casing?
1 mark
6d. What is the name of the process, that results in the base being manufactured?
1 mark
HELPFUL LINK http://www.technologystudent.com/equip1/vacform1.htm
LOGO / SYMBOL
MOULD
MDF BACK
6e. The mould for the casing is seen opposite. How is the mould ﬁnished, to ensure that it can be removed from the moulded ‘plastic’, after vacuum forming? 2 marks
HELPFUL LINK http://www.technologystudent.com/gprep07/vac2.html
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 51
HELPFUL LINK http://www.technologystudent.com/gprep07/vac3.html
6f. In the space below, explain the stages involved in the vacuum forming process, of the casing of the warning light. Use both labelled sketches and notes in your answer. 8 marks
NOTES SKETCHES
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 52
7a. Sliding doors have electromechanical systems to enable them to work. The two doors are shown below. Add to the drawing, a suitable mechanical system, that would allow the doors to be opened and closed, in the event of an electronic / electrical failure. Add explanatory notes and labels. 5 marks
NOTES
HELPFUL LINK http://www.technologystudent.com/sysprp7/sysq17.html
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2017 V.Ryan © 2017
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 53
7b. The sliding doors are to be updated again, so that they work automatically, the through a system of pulleys (shown in the diagram below).
(I) Calculate the Velocity Ratio of the pulley system. Include all your working out
2 marks
(ii). Calculate the RPM of pulley ‘B’. Include all your working out.
3 marks
A
B
HELPFUL LINK http://www.technologystudent.com/gears1/pulley3.htm
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 54
8a. Industrial wave soldering is a process, whereby circuit boards and their components, are solder, on a mass production line. This is the way thousands of circuits are manufactured.
Using the table below, explain each of the stages in the wave soldering process, adding notes and diagrams / sketches. The ﬁrst stage has been completed for you.
6 marks
NOTES / EXPLANATION | DIAGRAM /SKETCH
APPLICATION OF FLUX | 
The ﬁrst stage is the application of ﬂux. This is a substance that helps keep the circuit board clean, by preventing oxidisation, during the heating process. The ﬂux is sprayed in the form of a ﬁne mist, onto the underneath of the board, covering the tracks and exposed ‘pins’ of the components. | Mist of ﬂux sprayed by ﬂux applicator.
HEATING OF THE CIRCUIT BOARD | 
THE WAVE SOLDERING TANK | 
HELPFUL LINK http://www.technologystudent.com/pcb/wave1.html
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 55
8b. The two graphs shown below, visually represent signals. Name each of the graphs with the correct type of signal. 2 marks
SIGNAL: SIGNAL:
HELPFUL LINK http://www.technologystudent.com/elec1/anadig1.htm
TIME
VOLUME
ON ON ON |  |  |  |  |  | 
OFF |  | OFF |  | OFF |  | 
TIME
VOLTS
8c. A range of wind-up rechargeable devices exist, such as the torch seen opposite. Give three advantages of modern recharageable torches.
3 marks
HELPFUL LINK http://www.technologystudent.com/enerﬂsh/ensave1.html
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 56
(II) What is Kinetic Energy (1 mark)?
9a. The carriage of a roller coaster seen below is at the top of an incline. At any point it could roll downwards, gathering speed. What is potential energy?
(I) Potential energy is (1 mark):
(iii). The carriage at the bottom of the roller coaster incline has a special gear system. On the diagram, the gear system is marked A and B. What are the correct names for parts A and B ?
A
B
PART A: 1 mark
PART B:
1 mark
RYAN RAIL SYSTEMS
RYAN RAIL SYSTEMS
HELPFUL LINK http://www.technologystudent.com/sysprp08/quest1.html
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 57
10. Environmental damage, pollution and climate change, are serious global problems, aﬀecting everyone. Discuss some of the problems we face and potential solutions. 9 marks
HELPFUL LINK http://www.technologystudent.com/despro_ﬂsh/morals2.pdf Page 5 onwards
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 58
WHEEL
SIDE
BASE
HANDLE SIDE
5. The drawing below shows the basic solution to a children’s trolley, which stores building blocks.
HANDLE (DOWEL ROD)
The trolley has a ﬁxed handle, that is permanently in one position. The corners of the storage unit are ‘pinned and glued’, for speed of manufacture. The handle is plain, being manufactured from dowel.
The trolley is spray painted in a variety of colours.
PINNED AND GLUED JOINTS
SECTION B – TIMBERS
Answer ALL questions
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 59
5a. The children’s trolley, needs to be improved to include the following speciﬁcation points.
The trolley must:
(I) Have an ergonomically designed handle.
(I) The handle must fold ﬂat, so that the trolley can be stored, saving space.
(iii) The corner joints of the storage unit, need to be upgraded so that they are strong and can withstand ‘knocks’.
Use notes and/or sketches to show how the children’s trolley could be modiﬁed to satisfy the addition speciﬁcation points, listed above
Produce clear drawings / sketches, using the outline of the original design to show how the additional speciﬁcation points can be met.
6 marks
HELPFUL LINKS http://www.technologystudent.com/despro_3/wdjoints1.html http://www.technologystudent.com/despro_3/block1.html http://www.technologystudent.com/despro_3/ergotrol1.html
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 60
5b. The recycling bin shown opposite is suitable for a kitchen. It has three separate storage bins, for diﬀerent materials.
Describe TWO other ways in which this design meets the design requirements for a recycle bin.
4 marks
(I)
(II)
HELPFUL LINK http://www.technologystudent.com/rmprep09/prodal1.html
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 61
5c. The modern recycling bin seen below, is manufactured from MDF or PLYWOOD. Old plastic shopping bags can be ‘hung’ inside each compartment on hooks. There is a central compartment for used shopping bags. It is delivered to the customer as a ﬂat pack and can be assembled within ten minutes. It rests on casters for ease of movement. As it is wood based and can be recycled at the end of its useful working life.
(I) Explain why a ‘template’ is useful when manufacturing a number of these bins.
2 marks
HELPFUL LINK http://www.technologystudent.com/rmprep09/singl1.html
(I) Explain why a fretsaw or bandsaw could be useful when cutting the sides of the bin.
2 marks
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 62
HELPFUL LINK http://www.technologystudent.com/despro_ﬂsh/ﬁnish8.html
5d. The panels / sides of the bin are to be painted, producing a high quality ﬁnish.
(I) Using notes and sketches, describe the stages involved in preparing the surface of the ‘wood’ panels / sides and the application of a quality paint ﬁnish.
4 marks
(II) Why is the use of water based paints more environmentally friendly, than using oil / solvent based paints? 2 marks
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 63
(I) Describe 6 advantages of using CAD and CAM in the manufacture of large numbers of this design of bin. 6 marks
HELPFUL LINKS http://www.technologystudent.com/cam/cncman4.htm http://www.technologystudent.com/rmprep09/shop1.html
6a. A retailer has ordered a large number of the ‘wood’ based recycle bins. It has been decided to manufacture the bins using CAM, such as the CNC Router seen below. To start with, the sides are drawn using CAD software.
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 64
7a. The table below has been permanently ﬁxed together using plain mortise and tenon joints, as seen opposite.
The table has been found to be weak. Name and produce a labelled sketch, of a more sophisticated mortise and tenon joint, that is likely to strengthen the table. 5 marks
http://www.technologystudent.com/joints/mort1.htm HELPFUL LINKS http://www.technologystudent.com/joints/joints4.htm
http://www.technologystudent.com/joints/mort2.htm
www.technologystudent.com © 2018
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
V.Ryan © 2018

## Slide 65
The plain table top is to be modiﬁed. A rectangular acrylic window is to be added. The top is now composed of two rectangular pieces, accurately cut to size on a CNC router. They ﬁt perfectly together.
2 marks
300mm
400mm
A
B
150mm
7b. Calculate the total area of piece A, before ‘B’ is removed
7c. Calculate the area of piece B. 2 marks
7d. Calculate the area of A, after ‘B’ is removed. 1 mark
200mm
HELPFUL LINK http://www.technologystudent.com/pdf14/maths3.pdf Page 8
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 66
HELPFUL LINK http://www.technologystudent.com/rmﬂsh1/ebeech1.html
7e. European Beech has been selected for the manufacture of the table. Explain why this is a good choice. 4 marks
HELPFUL LINK http://www.technologystudent.com/rmﬂsh1/natwd1.html
7f. Name another natural wood that would be suitable for the manufacture of the table. Explain why you consider it to be suitable. 2 marks
NAME:
WHY SUITABLE:
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 67
8. The products shown below have been manufactured from ﬂexi-ply.
HELPFUL LINK http://www.technologystudent.com/despro_ﬂsh/ﬂexply1.html
(I) Why is ﬂexi-ply a suitable material for these shapes / forms of products? 5 marks
HELPFUL LINK http://www.technologystudent.com/prddes1/eames6.html
(II) Another way of producing curves in woods is to use layers of veneers / plywood and to ‘steam bend’. Describe the process called ‘steam bending’. 4 marks
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 68
9. Describe how natural wood can signiﬁcantly contribute to the sustainability of our use of materials. 9 marks
http://www.technologystudent.com/prddes1/susenv1.html HELPFUL LINKS http://www.technologystudent.com/prddes1/lifecy1.html
http://www.technologystudent.com/despro_ﬂsh/morals2.pdf Page 5 onwards
WORLD ASSOCIATION OF TECHNOLOGY TEACHERS https://www.facebook.com/groups/254963448192823/
www.technologystudent.com © 2018 V.Ryan © 2018

## Slide 69
ADD YOUR OWN TEXTILES SPECIFIC EXAMINATION QUESTIONS